|  | United Nations | ECE/TRANS/WP.29/2011/21 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2010 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

153rd session

Geneva, 8–11 March 2011

Item 4.10.5 of the provisional agenda

1958 Agreement – Consideration of draft Corrigenda

to existing Regulations submitted by GRE

Proposal for Corrigendum 1 to the 04 series of amendments to Regulation No. 19 (Front Fog Lamps)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-fourth session. It is based on ECE/TRANS/WP.29/GRE/2010/33 and ECE/TRANS/WP.29/GRE/2010/57, both not amended, and on informal document GRE-64-18, as reproduced in Annex VIII to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/64, para. 28).

Paragraph 14.1.5., correct to read:

"14.1.5.	Contracting Parties applying this Regulation may prohibit the fitting of devices, which do not meet the requirements of the 03 series of this Regulation:

14.1.5.1.	On vehicles for which type approval or individual approval is granted more than 24 months after the date of entry into force of the 03 series of amendments.

14.1.5.2.	On vehicles first registered more than 60 months after the date of entry into force of the 03 series of amendments."

Insert a new paragraph 14.2.2., to read:

"14.2.2.	Until 60 months after the date of entry into force of the 04 series of amendments to this Regulation with regard to the changes introduced by the 04 series of amendments concerning the photometric testing at reference luminous flux at approximately 13.2 volts, and in order to allow the Technical Services to update their testing equipment, no Contracting Party applying this Regulation shall refuse to grant approvals under this Regulation as amended by the 04 series of amendments where existing testing equipment is used with suitable conversion of the values, to the satisfaction of the authority responsible for type approval."

Paragraph 14.2.2. (former), renumbered as paragraph 14.2.3.

Annex 2, paragraph 2.2., line 6 of the table, correct to read:

"…

| Line 6 ***/ | - 2.5° | from 5° inwards to 10° outwards | 2,160 min | 1,890 min | All line |
| --- | --- | --- | --- | --- | --- |

…"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.