|  | United Nations | ECE/TRANS/WP.29/2011/76 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 7 April 2011 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

154th session

Geneva, 21–24 June 2011

Item 4.13.1 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda

to existing Regulations submitted by GRB

Proposal for Corrigendum 3 to the 02 series of amendments to Regulation No. 117 (Tyre rolling resistance, rolling noise and wet grip adhesion)

Submitted by the Working Party on Noise*

The text reproduced below was adopted by the Working Party on Noise (GRB) at its fifty-third session to clarify the provisions on the reproducibility of tyre measurements in laboratories. It is based on ECE/TRANS/WP.29/GRB/2011/4, as amended by paragraph 19 of the report (ECE/TRANS/WP.29/GRB/51, para. 19). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraphs 2.18.9., footnote 9, correct to read:

"9	Measurement reproducibility σm shall be estimated by measuring n times (where n ≥ 3), on a single tyre, the whole procedure described in paragraph 4. of Annex 6 as follows:

Where:

j	=	is the counter from 1 to n for the number of repetitions of each measurement for a given tyre,

n	=	number of repetitions of tyre measurements (n ≥ 3)."

Annex 6, paragraph 4.7., amend to read:

"4.7.	Allowance for machines exceeding σm criterion …"

Annex 6, paragraph 6.5., amend to read:

"6.5.	The laboratory shall ensure that, based on a minimum of three measurements, the machine maintains the following values of σm, as measured on a single tyre:

σm ≤ 0.075 N/kN for tyres of Classes C1 and C2

σm ≤ 0.06 N/kN for tyres of Class C3

If the above requirement for σm is not met, the following formula shall be applied to determine the minimum number of measurements n (rounded to the immediate superior integer value) that are required by the machine to qualify for conformance with this Regulation.

n = (σm / x)²

…"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208/, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.