|  | United Nations | ECE/TRANS/WP.29/GRE/2011/10 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 14 January 2011 Original: English English and French only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Lighting and Light-Signalling

Sixty-fifth session

Geneva, 28–31 March 2011

Item 5(h) of the provisional agenda

Collective amendments—Regulations Nos. 4, 6, 7,
 23, 38, 50, 77, 87, 91 and 119

Proposal for Supplement 16 to Regulation No. 38 (Rear fog lamps)

Submitted by the expert from the Working Party "Brussels 1952"*

The text reproduced below was prepared by the expert from the Working Party "Brussels 1952" (GTB) to introduce into the Regulation provisions for the use of light-emitting diode (LED) light sources according to the draft Regulation (Regulation No. XXX: ECE/TRANS/WP.29/2010/44 and Corr.1). The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

- Proposal

Paragraph 1.3., amend to read:

"1.3. 	"Rear fog lamps of different types" means ...

…

(b)	The characteristics of the optical system (levels of intensity, light distribution angles, category of filament lamp light source, light source module, etc.);

A change of the colour of the filament lamp light source or the colour of any filter does not constitute a change of type."

Insert a new paragraph 1.4., to read:

"1.4.	References made …for type approval.

References made in this Regulation to standard (étalon) LED light source(s) and to Regulation No. XXX shall refer to Regulation No. XXX and its series of amendments in force at the time of application for type approval."

Paragraph 2.2.2., amend to read:

"2.2.2.		a brief … light sources:

(a)	The category … ; and/or

(b)	The category or categories of LED light source(s) prescribed; this LED light source category shall be one of those contained in Regulation No. XXX and its series of amendments in force at the time of application for type approval; and/or

(c)	The light source module specific identification code.

(d)	For a rear fog lamp of category F2, a concise description of the variable intensity control."

Paragraph 3.2., amend to read:

"3.2.	With the …indicating:

(a)	The category or categories of filament lamp light source prescribed; and/or

(b)	the light source module specific identification code."

Paragraphs 5.5. to 5.5.3., amend to read:

"5.5.	In the case of replaceable light sources:

5.5.1.	Any category or categories of filament lamp(s) light source(s) approved according to Regulation No. 37 and/or Regulation No. XXX may be used, provided that no restriction on the use is made in Regulation No. 37 and its series of amendments in force at the time of application for type approval or in Regulation No. XXX and its series of amendments in force at the time of application for type approval.

5.5.2.	The design of the device shall be such that the filament lamp light source can be fixed in no other position but the correct one.

5.5.3. 	The filament lamp light source holder shall conform to the characteristics given in IEC Publication 60061. The holder data sheet relevant to the category of filament lamp light source used, applies."

Paragraph 7.1.1., amend to read:

"7.1.1.	In the case of a…standard filament lamp light source of the category prescribed for the device, supplied with the voltage:

(a) 	In the case of filament lamp(s), that is necessary to produce the reference luminous flux required for that category of filament lamp,

(b) 	In the case of LED light sources of 6.75 V, 13.5 V or 28.0 V; the luminous flux value produced shall be corrected. The correction factor is the ratio between the objective luminous flux and the mean value of the luminous flux found at the voltage applied."

Annex 3, paragraph 5.2., amend to read:

"5.2.		For replaceable filament lamp light source(s):

When equipped with filament lamp(s) light source(s) at 6.75 V, 13.5 V or 28.0 V, the luminous intensity values produced shall be corrected. For filament lamps the correction factor is the ratio between the reference luminous flux and the mean value of the luminous flux found at the voltage applied (6.75 V, 13.5 V or 28.0 V).  When equipped with LED light source(s) at 6.75 V, 13.5 V or 28.0 V; the luminous flux value produced shall be corrected. The correction factor is the ratio between the objective luminous flux and the value of the luminous flux found at the voltage applied.

The actual luminous fluxes of each filament lamp light source used shall not deviate more than 5 per cent from the mean value.

Alternatively and in case of filament lamps only, a standard filament …."

Annex 4, paragraph 1.2.2., amend to read:

"1.2.2.		If, in the case of a …standard filament lamp light source."

Annex 5, paragraphs 1.2.2., amend to read:

"1.2.2.		If, in the case of a …standard filament lamp light source."

II.	Justification

1.	At its sixty-second session, GRE adopted ECE/TRANS/WP.29/GRE/2009/55, a draft Regulation for LED light sources (Regulation No. XXX), where it is intended to provide an additional light source option of replaceable, approved LED light sources.

2.	This proposal aims to incorporate LED light sources into Regulation No. 38 as an alternative replaceable light source. Therefore all parts in the text referring to "filament lamps" have been replaced by the more general wording "light source" to allow in future both types of approved light source categories to be used. Where necessary a distinction between both types has been made and references to the appropriate light source Regulations (Regulation No. 37 and Regulation No. XXX) have been added.

3.	This proposal is part of a collective amendment comprising the following Regulations Nos. 4, 6, 7, 23, 38, 50, 77, 87, 91 and 119.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010-2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.