|  | United Nations | ECE/TRANS/WP.29/2012/50 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 12 April 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

157th session

Geneva, 26-29 June 2012

Item 4.9.4 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulations submitted by GRRF

Proposal for Supplement 2 to the 02 series of amendments to Regulation No. 64 (Temporary use spare wheels/tyres, run flat tyres, run flat system and tyre pressure monitoring system)

Submitted by the Working Party on Brakes and Running Gear *

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its seventy-second session inserting a reference to Regulation No. 54 into Regulation No. 64 and adapting the speed limit of type 4 spare units. It is based on ECE/TRANS/WP.29/GRRF/2012/13, amended as indicated in Annex V to the report (ECE/TRANS/WP.29/GRRF/72, para. 35). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 5.1.1., amend to read:

"5.1.1.	Tyres intended for use as part of a temporary-use spare unit as defined in paragraph 2.10., shall be approved in accordance with Regulations Nos. 30 or 54."

Paragraph 5.1.4.1., amend to read:

"5.1.4.1.	An 80 km/h maximum speed warning symbol arranged in accordance with the diagram below shall be permanently displayed on the outer face of the wheel in a prominent position:

…

The requirements of this paragraph shall apply to types 1, 2 and 3 temporary-use spare unit as defined in paragraphs 2.10.1., 2.10.2. and 2.10.3."

Paragraph 5.1.4.1.1, amend to read:

"5.1.4.1.1.	An 120 km/h maximum speed warning symbol arranged in accordance with the diagram below shall be permanently displayed on the outer face of the wheel in a prominent position.

…

Upper case letters … All text shall be enclosed in a border and be on a background of contrasting colour.

For a type 4 temporary-use spare unit as defined in paragraph 2.10.4, either the requirements of this paragraph or the requirements of paragraph 5.1.4.1. shall apply, at the request of the vehicle manufacturer."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.