| Submitted by the expert from OICA | Informal document No. GRE-67-26 (67th GRE, 26-29 March 2012 agenda item 4(a) (i)) |
| --- | --- |

Proposal for Supplement 10 to the 04 series of amendments to Regulation No. 48 (Installation of lighting and light-signalling devices)

The text reproduced below was prepared by the expert from OICA to improve the wording of the informal document GRE-67-08 submitted by France. The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

- Proposal

Paragraph 6.6.8, amend to read as follows:

6.6.8.   Tell-tale

Circuit-closed tell-tale mandatory. Flashing warning light, which can operate in conjunction

with the tell-tale(s) specified in Paragraph 6.5.8.

Circuit-closed tell-tale is not required when the turn signal tell-tales, that otherwise operate independently, flash simultaneously as hazard warning tell-tale.

II.	Justification

This proposal aims to clarify the wording of the informal document GRE-67-08 submitted by France.