|  | United Nations | ECE/TRANS/WP.29/GRSG/2012/17 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 19 July 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

103rd session

Geneva, 2–5 October 2012

Item 6 of the provisional agenda

Regulation No. 67 (Equipment for liquefied petroleum gases (LPG))

Proposal for a Corrigendum to Regulation No. 67 (Equipment for liquefied petroleum gases)

Submitted by the expert from the European Liquefied Petroleum Gas Association*

The text reproduced below was submitted by the expert from European Liquefied Petroleum Gas Association (AEGPL) clarifying the provisions on the aerostatic pressure during the external leakage test of Class 0 components. The modifications to the existing text of the Regulation are marked in bold characters.

I.	Proposal

Annex 15, paragraph 5.3., table 3, amend to read:

"Table 3: The classification and leakage test pressures according to the classification:

| Classification of component | Classification pressure [kPa] | Test pressure for leakage test [kPa] |
| --- | --- | --- |
| Class 0 | WP | 1.5 WP |
| Class 1 | 3,000 | 4,500 |
| Class 2A | 120 | 180 |
| Class 2 | 450 | 675 |
| Class 3 | 3,000 | 6,750 |

"

II.	Justification

1.	Table 3 of Annex 15, which sets out the test pressures for external leakage test, does not contain any value for Class 0 components.

2.	The proposal clarifies the aerostatic pressure which shall be reached during the external leakage test (specified in paragraph 5 of Annex 15) of Class 0 components, in line with the provisions of paragraph 5.3.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.