|  | United Nations | ECE/TRANS/WP.29/2013/16 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 December 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

159th session

Geneva, 12-15 March 2013

Item 4.9.4 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 5 to the 04 series of amendments to Regulation No. 19 (Front fog lamps)

Submitted by the Working Party on Lighting and Light Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light Signalling (GRE) at its sixty-eighth session (ECE/TRANS/WP.29/GRE/68, para. 31). It is based on ECE/TRANS/WP.29/GRE/2012/32, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraph 6.4.2.2., amend to read:

"6.4.2.2.	The beam shall produce on this aiming screen, over a width of not less than 5.0 degrees on both sides of the line v, a symmetrical and substantially horizontal cut-off to enable visual vertical adjustment. In the case that visual aim leads to problems or ambiguous positions, the measurement of the cut-off quality and the instrumental method as specified in paragraphs 4. and 5. of Annex 9 shall be applied."

Paragraph 6.4.2.3., should be deleted.

Paragraph 6.4.2.4. (former), renumber as paragraph 6.4.2.3.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.