|  | United Nations | ECE/TRANS/WP.29/2013/83 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 16 August 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

161st session

Geneva, 12-15 November 2013

Item 4.6.16 of the provisional agenda

1958 Agreement – Consideration of draft amendments 
to existing Regulations submitted by GRE

Proposal for Supplement 17 to Regulation No. 50 (Position, stop, direction indicator lamps for mopeds and motorcycles)

Submitted by the Working Party on Light and Light-signalling*

The text reproduced below was adopted by the Working Party on Light and Light-signalling (GRE) at its sixty-ninth session (ECE/TRANS/WP.29/GRE/69, para. 19). It is based on ECE/TRANS/WP.29/GRE/2013/17 not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Insert a new paragraph 3.2.4., to read:

"3.2.4.	In the case of a non-replaceable filament lamp(s) or light source module(s) equipped with non-replaceable filament lamp(s): the documents according to paragraph 6.6. of this Regulation."

Insert a new paragraph 6.6., to read:

"6.6.	In the case of non-replaceable filament lamp(s) or light source module(s) equipped with non-replaceable filament lamp(s), the applicant shall annex to the type approval documentation a report (by the light source manufacturer indicated in the type approval documentation), acceptable to the Authority responsible for type approval, that demonstrates compliance of these
non-replaceable filament lamp(s) with the requirements as specified in paragraph 2.11. of IEC 60809, Edition 3."

Insert new paragraphs 10.2. to 10.2.2.2., to read:

"10.2.	In the case of non-replaceable filament lamp(s) or light source module(s) equipped with non-replaceable filament lamps:

10.2.1	A report (by the light source manufacturer indicated in the type approval documentation) shall demonstrate compliance of these non-replaceable filament lamp(s) with lifetime requirements and, in the case of colour coated filament lamps, also with colour endurance requirements, as specified in paragraph 2.11. of IEC 60809, Edition 3;

10.2.2.	At any conformity of production check:

10.2.2.1.	The holder of the approval mark shall demonstrate the use in normal production and show the identification of the non-replaceable filament lamp(s) as indicated in the type approval documentation;

10.2.2.2.	In the case where doubt exists in respect to compliance of the non-replaceable filament lamp(s) with lifetime requirements and/or, in the case of colour coated filament lamps, with colour endurance requirements, as specified in paragraph 2.11. of IEC 60809, Edition 3, conformity shall be checked (by the light source manufacturer indicated in the type approval documentation) as specified in paragraph 2.11. of IEC 60809, Edition 3."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.