Table 1: Limit value Draft for Chinese noise regulation (GB 1495)

| Vehicle Category | Sub-category | Limit value (Phase 1st) | Limit value (Phase 2nd) |
| --- | --- | --- | --- |
| M1* | GVM≤2 500 kg | 72 | 71 |
|  | GVM>2 500 kg | 73 | 72 |
| M2** | GVW≤3 500 kg | 74 | 73 |
|  | GVW>3 500 kg | 76 | 75 |
| M3** | GVM≤7 500 kg | 78 | 77 |
|  | 7 500 kg＜GVM≤12 000 kg | 80 | 79 |
|  | GVM＞12 000 kg | 81 | 80 |
| N1* | GVM≤2 500 kg | 73 | 72 |
|  | GVM>2500 kg | 74 | 73 |
| N2** | GVW≤7 500 kg | 78 | 77 |
|  | GVW>7 500 kg | 79 | 78 |
| N3** | GVW≤17 000 kg | 81 | 80 |
|  | GVW>17 000 kg | 82 | 81 |

Additional items (All the additional items can be accumulated.):

- *Increased by 1 dB(A) for M1 (GVW≤2 500kg) with more than one axle drive during the test or with middle (rear) engine and rear axle drive; increased by 1 dB(A) for M1 (GVW>2 500kg) and N1 with more than one axle drive during the test or with the single rear axle drive;

- *Increased by 1 dB(A) for M1 with the PMR values higher than 120 kW/t and equal or lower than 160 kW/t, and increased by 2dB(A) with the PMR values higher than 160 kW/t;

3. **Increased by 1 dB(A) for M2, M3, N2, N3 with more than one drive axle during the test;

4. **Increased by 1 dB(A) for M2, M3, N2, N3 with more than two axles.

Table 2: Suggestions for the limit values of ECE R51 / 03 series

| Vehicle Category | Sub-category | Limit value (Phase 1st) | Limit value (Phase 2nd) |
| --- | --- | --- | --- |
| M1 | PMR ≤ 120 kW/t | 72 | 71 |
|  | 120 < PMR ≤ 160 kW/t | 73 | 72 |
|  | PMR > 160 kW/t | 74 | 73 |
|  | PMR > 160 kW/t + middle (rear) engine+ rear axle drive | 75 | 74 |
|  | GVW≤ 2 500kg and height of R-point> 800mm | 74 | 72 |
|  | GVW> 2 500kg and height of R-point> 850mm |  |  |
| M2 | GVW ≤ 3 500 kg | 74 | 73 |
|  | GVW > 3 500 kg | 76 | 75 |
| M3 | GVM≤7 500 kg | 78 | 76 |
|  | 7 500 kg <GVM≤12 000 kg | 80 | 79 |
|  | GVM>12 000 kg | 81 | 80 |
| N1 | GVM≤2 500kg | 73 | 72 |
|  | GVM≤2 500kg and height of R point> 800mm | 74 | 72 |
|  | GVM>2 500kg | 74 | 73 |
| N2 | GVW≤7 500 kg | 78 | 77 |
|  | GVW>7 500 kg | 79 | 78 |
| N3 | Pn≤225 kW | 81 | 80 |
|  | Pn>225 kW | 82 | 81 |

Additional items (All the additional items can be accumulated.):

For off-road use and with a maximum authorized mass above 2 tons, the limit values shall be increased by 2 dB(A) for M3 and N3 vehicles category and 1 dB for any other vehicle category.