## Slide 1: Progress report of the informal group on REC
65th GRPE, 17 January 2013
Henk Baarbé
Informal document No. GRPE-65-38
(65th GRPE, 15 - 18 January 2012, agenda item 4(b))
Transmitted by WLTP-DTP

## Slide 2: State of Play
  Draft regulation almost complete
  Many editorial improvements still necessary
  A number of outstanding issues to be solved before the June GRPE meeting
  Several outstanding issues solved yesterday
  Main remaining outstanding issues presented today to GRPE.

## Slide 3: Main outstanding issues
NOx reduction performance of NOx reduction REC
Agreement on measuring NOx in WHTC, best representing urban driving conditions for trucks and buses where NOx reduction is most needed.
Agreement on performance requirement: 60 % reduction over WHTC for trucks and buses (on road vehicles)
Since NOx reduction performance of RECs for installation on NRMM is measured in NRTC, 60% is then less challenging due to on average higher engine loads.
Discussion:
Higher NOx reduction requirement for REC for NRMM, e.g.70%?
One contracting party still wants this 70% for REC for NRMM. Most others have expressed they can accept 60%.

## Slide 4: Main outstanding issues
Direct NO2 emissions.
Many DPF now successfully being applied are of the continuously regenerating type, typically showing a considerable increase in direct NO2 emissions, undesirable in situations with AAQ problems for NO2
Options already agreed upon:
Evaluation of direct NO2 during WHTC/NRTC.
Separate class of REC with zero increase of direct NO2
Combined PM and NO2 REC (class 4) pose no NO2 problem due to decrease of NOx
Cap on direct NO2 increase for continuously regenerating traps.
Discussion:
Should the cap be e.g. 20% or 30%?
Many CRT type REC being applied now > 30% direct NO2. 20% cap will lead to more complex and expensive ways of (active) regeneration, also for situations where NO2 poses no AAQ problem.
One Contracting Party insists on 20% increase max, most others and industry favour 30%

## Slide 5: How to proceed further
Many further improvements still to be drafted and discussed
Informal group planned for 19 and 20 February to do this. Switzerland has kindly offered to host this meeting.
Ambition is still to submit a formal proposal for a Regulation to GRPE in June 2013, together with an informal proposal for an amendment 01.
Requested: a half day informal group meeting in conjunction with the GRPE in June
Note: our project is not on the work programme (list of New Regulations) of WP29

## Slide 6: Thank you for your attention
Henk Baarbé