|  | United Nations | ECE/TRANS/WP.15/AC.1/2014/6 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 20 December 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Committee of Experts and the

Working Party on the Transport of Dangerous Goods

Bern, 17-21 March 2014

Item 2 of the provisional agenda

Tanks

Chapter 6.10 Vacuum-operated waste tanks - Explosion-pressure proof design of vacuum-operated tanks as an alternative to flame traps

Transmitted by the Government of Germany,

Summary

Executive summary: The aim of this proposal is to ensure that the provisions concerning the protection of vacuum-operated waste tanks against fire or the risk of explosion when being bottom filled or discharged using vacuum pumps/exhausters are clearly worded.

Action to be taken: Include an operating provision in RID/ADR Chapter 4.5.

Related documents: ECE/TRANS/WP.15/AC.1/2013/12; ECE/TRANS/WP.15/AC.1/2013/36; Report of the working group on tanks ECE/TRANS/WP.15/AC.1/132/Add.1 paragraphs 3 and 4 and informal document INF.60 of the Joint Meeting (September 2013

Introduction

1.	At the last RID/ADR/ADN Joint Meeting (Geneva, 17 to 27 September 2013), the working group on tanks discussed France's proposal ECE/TRANS/WP.15/AC.1/2013/36. France was concerned that when operating vacuum pumps/exhausters with the possible generation of sparks (without flame arresters), people might be put at risk from an explosion.

2.	The biggest risk of explosion propagation occurs mainly when filling starts and when discharging finishes, if the tank and discharge pipe are not filled with liquid.

3.	On the basis of his presentation (informal document INF.60), the representative of Germany agreed to draft an operating provision for the use of explosion pressure proof tanks for flammable liquids to reduce the risk of explosion propagation.

Proposal

4.	Include a new operating provision in RID/ADR Chapter 4.5.

"4.5.2.6	When suction filling or emptying flammable liquids from or into a non explosion 		pressure shock resistant tank, it shall be ensured that if vacuum pumps/exhausters 		that might create sparks are used (without flame arresters), these shall only be in 		operation when the connecting pipe is completely filled with liquid or the vacuum-		operated tank is inerted."

5.	As a consequence, the end of 4.5.2.1 should be amended to read:

"...by the requirements of 4.5.2.2 to 4.5.2.6 below.".

______________

# Footnotes

In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94, ECE/TRANS/2012/12, programme activity 02.7 (A1c)).

Circulated by the Intergovernmental Organisation for International Carriage by Rail (OTIF) under the symbol OTIF/RID/RC/2014/6.