|  | United Nations | ECE/TRANS/WP.29/2014/15 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 18 December 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

162nd session

Geneva, 11-14 March 2014

Item 4.9.3 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 23 to the 02 series of amendments to Regulation No. 7 (Position, stop and end-outline lamps)

Submitted by the Working Party on Lighting and Light-Signalling *

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its seventieth session (ECE/TRANS/WP.29/GRE/70, para. 28). It is based on ECE/TRANS/WP.29/GRE/2013/42, not amended, and on ECE/TRANS/WP.29/GRE/2013/48, as amended by Annex VI to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraph 6.1., amend to read:

"6.1.	The light emitted by each of the two devices supplied shall be in the reference axis, of not less than the minimum intensity and of not more than the maximum intensity specified below:

|  | Minimum luminous intensity in cd | Maximum luminous intensity in cd when used as |
| --- | --- | --- |
|  |  | Single lamp | Lamp (single) marked "D" paragraph (4.2.2.6.) |
| 6.1.1. Front position lamps, front end-outline marker lamp A or AM | 4 | 140 | 70 |
| 6.1.2. Front position lamps incorporated in a headlamp or front fog lamp | 4 | 140 | - |
| 6.1.3. Rear position lamps, rear end-outline marker lamp 6.1.3.1. R, R1 or RM1 (steady) | 4 | 17 | 8.5 |
| 6.1.3.2. R2 or RM2 (variable) | 4 | 42 | 21 |
| 6.1.4. Stop-lamps |  |  |  |
| 6.1.4.1. S1 (steady) | 60 | 260 | 130 |
| 6.1.4.2. S2 (variable) | 60 | 730 | 365 |
| 6.1.4.3. S3 (steady) | 25 | 110 | 55 |
| 6.1.4.4. S4 (variable) | 25 | 160 | 80 |

"

Paragraph 6.2.4.2., amend to read:

"6.2.4.2.	If a rear position lamp and/or a rear end-outline marker lamp is reciprocally incorporated with a stop-lamp producing either steady or variable luminous intensity, the ratio between the luminous intensities actually measured of the two lamps when turned on simultaneously at the intensity of the rear position lamp or end-outline marker lamp when turned on alone should be at least 5: 1 in the field delimited by the straight horizontal lines passing through ±5° V and the straight vertical lines passing through ±10° H of the light distribution table.

If the one or both of the two reciprocally incorporated lamps contain(s) more than one light source and is (are) considered as a single lamp, the values to be considered are those obtained with all light sources in operation;"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.