|  | United Nations | ECE/TRANS/WP.29/GRRF/76/Add.1 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 21 May 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Seventy-sixth session

Geneva, 17–21 February 2014

Report of the Working Party on Brakes and Running Gear
on its seventy-sixth session

Addendum

Insert a new paragraph 24bis, to read:

"24bis.	The expert from the Russian Federation presented GRB-59-02 proposing a tyre rolling resistance test results evaluation using a mathematical algorithm, to be added as an alternative to the existing one in the text of the Regulation. He also presented the results of a validation study of the proposed algorithm for tyres of the C1 category performed in France, in cooperation with the Russian Federation (GRB-59-07 and GRB-59-08). GRRF noted that this proposal may be submitted by GRB to WP.29 as a supplement to UN Regulation No. 117. GRRF recommended further steps for a better understanding of the proposed method's sensitivity, suggesting: (i) extending the validation study for tyres of categories C2 and C3 and (ii) verifying the application of the proposed alternative in the conditions of the conformity of production. The GRRF Chair invited the experts to provide their comments on the proposal to the GRB secretariat with a copy to the expert from the Russian Federation."