Proposal for amendments to 
ECE/TRANS/WP.29/GRRF/2014/19
on Regulation No. 79 (Steering equipment)

The amendments compared to   ECE/TRANS/WP.29/GRRF/2014/19   are indicated in red text

I.	Proposal

Insert a new paragraph 5.3.1.6., to read:

"5.3.1.6.	The requirements of for the braking performance in paragraphs 5.3.1.4. and 5.3.1.5. above shall not apply when the prescribed secondary braking performance defined in Paragraph 3 of Annex 3 of this Regulation  can be achieved by the use of muscular energy alone."

Paragraph 5.3.1.6. (former), renumber as 5.3.1.7.

II.	Justification

1.	The current text of Annex 3 of UN Regulation No. 79 covers requirements to be met in case the braking and the steering systems have the same energy source. However these requirements are not aligned with those of UN Regulation No. 13-H. Paragraph 1.1.2. of Annex 4 to UN Regulation No. 13-H requires the capacity of a certain number of sudden stops after the energy source failed ONLY in the case where the secondary braking performances cannot be met without energy assisting the muscular energy:

"1.1.2.		However, the energy storage devices shall not be required to be of a prescribed capacity if the braking system is such that in the absence of any energy reserve it is possible with the service brake control to achieve a braking performance at least equal to that prescribed for the secondary braking system;"

2.	The current text of the provisions in UN Regulation No. 79 could be interpreted as the required number of sudden stops that must be achieved irrespective of the service braking design, i.e. even in the case of assisted braking system.

3.	This proposal is an attempt to clarify and align the wording of UN Regulation No. 79 with UN Regulation No. 13-H.

4. 	The fact, that in case of “a failure in the energy supply, the steering system shall have priority” remains valid.