## Slide 1: Background of the Proposals for amending R49 Rev 6 (ECE/ TRANS/WP.29/GRPE/2015/03 GRPE-70-06 and GRPE-70-07)
Informal document GRPE-70-24
(70th GRPE, 15-16 January 2015
agenda item 4(a))

## Slide 2: History
GRPE adopted in June 2014 a series of amendments to R49 rev.6
These amendments included a complete deletion of the urea consumption monitoring. This possible deletion was based on the general existence of close-loop systems in Heavy-Duty engines and vehicles.
In the meantime, it appeared that some Light Commercial vehicles were not equipped with such system, thereby creating a possible loop-hole in the Regulation.
The present proposals aim at introducing an alternative to the deletion of the urea consumption monitoring

## Slide 3: List of the amendments already proposed and adopted by GRPE in June 2014
Transposing the latest EU OTLs and their date of application
Improvement of the definition of CDmin
Stop-start and hybrid vehicles – OBD changes
Alternative service mode for LNG dual-fuel vehicles

## Slide 4: New Amendments proposed to GRPE
It is proposed to keep at stage C the fifty per cent threshold value required for reagent consumption monitoring in stage A
  Rationale: with the currently available sensor technology an effective inducement is already observed in the field by enforcing the stage A measures .
It is proposed at improving the neutrality of the requirements as regards the technology that may be used for monitoring the reagent consumption
  Rationale: The monitoring time requirement that is considered as necessary was not achievable with the two monitors currently specified. It is achievable with other technologies.
It is proposed to align the transitional provision with the one contained in the “General Guidelines for UN regulatory procedures and transitional provisions in UN Regulations” (document ECE-TRANS-WP29-1044r1e)