## Slide 1: Information on mandatory fitting of advanced safety systems in Japan
Engineering Policy Division
Road Transport Bureau
MLIT Japan
GRRF Meeting February 2015
Informal document GRRF-79-14
(79th GRRF, 16 – 20 February 2015,
agenda item 11)
Submitted by the expert from Japan

## Slide 2: Contents
Introduction
Mandatory fitting of advanced brake systems for motorcycles
Mandatory fitting of Lane Departure Warning Systems for heavy duty vehicles

## Slide 3
Introduction

## Slide 4
Introduction –The meaning of this presentation-
In Japan, the number of traffic accident fatalities is 4,113 in 2014. It is difficult to achieve the target of our government “Reduce the fatalities by traffic accidents to less than 2,500 by the year 2018".
Therefore additional vehicle safety measures are needed.
Specifically,
  Motorcycles: In Japan, while the number of fatalities on four-wheel vehicles has decreased by 52% from 10 years ago, the number of fatalities on two-wheel vehicles* has decreased by only 38%. Furthermore the number of fatalities per two-wheel vehicles is 4.7 times that of per four-wheel vehicles in 2013.
  Heavy duty vehicles: Many heavy duty vehicles cause critical accidents on highways. The damages of accidents caused by heavy duty vehicles are more serious than others.
In terms of the above mentioned, MLIT published new national regulations for mandatory fitting of ABS/CBS for motorcycles and LDWS for heavy duty vehicles, in line with the technical requirements in UN regulations.
  *Moped (type 1) are excluded.

## Slide 5: Introduction –Traffic accidents in Japan-
Chart: 
| 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Accidents | 42.5944 | 52.1481 | 63.5056 | 72.088 | 71.808 | 70.029 | 65.9283 | 58.6713 | 49.0452 | 47.2938 | 47.1041 | 46.0649 | 46.4037 | 47.1573 | 47.6677 | 48.5578 | 50.2261 | 52.6362 | 51.8642 | 55.2788 | 57.919 | 59.0723 | 61.4481 | 66.1363 | 64.3097 | 66.2392 | 69.5346 | 72.4678 | 72.9461 | 76.1794 | 77.1085 | 78.0401 | 80.3882 | 85.0371 | 93.195 | 94.7253 | 93.695 | 94.8281 | 95.2709 | 93.4339 | 88.7257 | 83.2691 | 76.6382 | 73.7628 | 72.5903 | 69.2056 | 66.5138 | 62.9021 | 57.3465
Fatalities | 13904 | 13618 | 14256 | 16257 | 16765 | 16278 | 15918 | 14574 | 11432 | 10792 | 9734 | 8945 | 8783 | 8466 | 8760 | 8719 | 9073 | 9520 | 9262 | 9261 | 9317 | 9347 | 10344 | 11086 | 11227 | 11109 | 11452 | 10945 | 10653 | 10684 | 9943 | 9642 | 9214 | 9012 | 9073 | 8757 | 8396 | 7768 | 7425 | 6927 | 6403 | 5782 | 5197 | 4968 | 4922 | 4663 | 4411 | 4373 | 4113
Injuries | 51.7775 | 65.5377 | 82.8071 | 96.7 | 98.1096 | 94.9689 | 88.9198 | 78.9948 | 65.142 | 62.2467 | 61.3957 | 59.3211 | 59.4116 | 59.6282 | 59.8719 | 60.7346 | 62.6192 | 65.4822 | 64.4321 | 68.1346 | 71.233 | 72.2179 | 75.2845 | 81.4832 | 79.0295 | 81.0245 | 84.4003 | 87.8633 | 88.1723 | 92.2677 | 94.2204 | 95.8925 | 99.0676 | 105.0399 | 115.5707 | 118.1039 | 116.8029 | 118.1681 | 118.3616 | 115.7115 | 109.8566 | 103.4653 | 94.5703 | 91.1215 | 89.6294 | 85.461 | 82.5396 | 78.1494 | 70.9989
Fatalities in 1970: 16,765
Fatalities in 2014: 4,113
Injuries in 1970: 981,096
Injuries in 2014: 709,989
Number of traffic accidents / fatalities / injuries
(National Police Agency of Japan)

## Slide 6
Mandatory fitting of advanced brake systems* for motorcycles
*Advanced brake systems: Anti-lock Brake Systems (ABS) and Combined Brake Systems (CBS)

## Slide 7: Motorcycles –Scope and Effective dates-
Scope
  Motorcycles* (125cm3 < engine capacity )
  Mopeds (type 2) (50cm3 < engine capacity ≤ 125cm3)
  *Enduro and Trial motorcycles are excluded.
Effective dates
  New types: October 2018
  All new vehicles: October 2021
(Issued: January 22 2015)

## Slide 8
Category | Engine Capacity: c[cm3] | Example | Technical inspection | Highway | License
Motorcycle (normal) | 400<c |  | Yes | Yes | Large
 | 250<c≤400 |  |  |  | Normal
Motorcycle (light) | 125<c≤250 |  | No |  | 
Moped (type 2) | 50<c≤125 |  |  | No | Small
Moped (type 1) | c≤50 |  |  |  | Moped
Motorcycles –Category in Japan-

## Slide 9: Motorcycles –Requirements and Estimated effect-
Requirements
Category | Mandatory fitting
Motorcycle (normal) | ABS*
Motorcycle (light) | 
Moped (type 2) | ABS* or CBS*
Moped (type 1) | -
  * ABS and CBS shall meet performance requirements in UN regulation No. 78.
194 people at most can be saved annually by mandatory fitting of advanced brake systems for motorcycles.
Estimation by Government of Japan

## Slide 10
Mandatory fitting of Lane Departure Warning Systems for heavy duty vehicles

## Slide 11: Heavy vehicles –Scope and Requirements-
Scope
  M2*, M3*, N2, N3
  *Coach only.
Requirements
  Vehicles shall be equipped with Lane Departure Warning Systems (LDWS) in accordance with UN regulation No. 130.
125 people at most can be saved annually if all vehicles fit LDWS.
Estimation by Government of Japan

## Slide 12: Heavy vehicles –Effective dates (1)-
Effective dates*
*On the same dates, mandatory fitting of Advanced Emergency Brake Systems (AEBS) 01 series will be come into force in Japan.
(Issued: January 22 2015)

## Slide 13: Heavy vehicles –Effective dates (2)-
* Vehicles without air suspension in Europe: (New types) Nov. 2016, (All new vehicle) Nov. 2018
*
*

## Slide 14
Thank you for your attention!
More Information?
  Atsushi KASAI
  Engineering Policy Division
  Road Transport Bureau
  MLIT Japan
  Phone: +81-3-5253-8591
  E-mail: kasai-a2d9@mlit.go.jp