|  | United Nations | ECE/TRANS/WP.29/GRSP/2015/13 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 27 February 2015 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Passive Safety

Fifty-seventh session

Geneva, 18-22 May 2015

Item 7 of the provisional agenda

Regulation No. 16 (Safety-belts)

Proposal for Supplement 6 to the 06 series of amendments to Regulation No. 16 (Safety-belts)

Submitted by the expert from the Netherlands *

The text reproduced below was prepared by the expert from the Netherlands aimed at clarifying the provisions for the approval of "general-use" safety-belts. The modifications to the current text of UN Regulation No. 16 are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 7.7.1., amend to read:

"7.7.1.	The belt assembly shall be mounted on a trolley equipped with the seat and the general anchorages as defined in Annex 6 to this Regulation. However, if the belt assembly is intended ... the maximum number of real anchorage points."

Annex 1B, item12, amend to read:

"12.	Approval granted/refused/extended/withdrawn2 for fixation to the general use anchorage positions as defined in Annex 6 to this Regulation/for use in a particular specific vehicle or in particular specific types of vehicles2,4 "

II.	Justification

1.	The current proposal aims to clarify the term "general use"-safety-belt (Annex 1B, item 12).

2.	The expert from the Netherlands had noted that the current understanding of "general use"-safety belt is misleading and suggests an allowance of installation that does not exist.

3.	Type approved safety-belts of this kind, should be attached to the anchorage point according to the coordinates specified in Annex 6 of this Regulation; an installation outside these coordinates is not permitted.

4.	The current proposal aims at providing clearer wording and a better correspondence between paragraph 7.7.1. and the Communication sheet/approval certificate.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.