## Slide 1
Progress Report of the
VIAQ (Vehicle Interior Air Quality)
Informal Working Group
Submitted by the VIAQ Chair and Secretary
10 June 2016
Report to the 73rd GRPE session
Informal document GRPE-73-25
73rd GRPE, 6-10 June 2016,
agenda item 13

## Slide 2
WP.29 Mandate(ECE/TRANS/WP.29/1112)
AC.3 endorsed the proposed action plan to, in a first stage, collect information, review existing standards and develop recommendations.
End of mandate : November 2017
GRPE Adoption(ECE/TRANS/WP.29/GRPE/70)
GRPE adopted the proposals for terms of reference to the IWG on VIAQ as reproduced in Annex VI of this report.
Review of VIAQ Terms of Reference
The scope of the work is to develop a recommendation (R.E.3, S.R.1, or a new Mutual Resolution) to harmonize test procedures of interior air emissions emitted/generated from interior materials
VIAQ Background, ToR and Mandate
VIAQ Background
Notes: 2

## Slide 3
VIAQ IWG Meetings since last GRPE
4th VIAQ IWG Meeting
Beijing, China, 30th – 31st March 2016 (VIAQ-04-11)
5th VIAQ IWG Meeting
Geneva, Switzerland, 8th June 2016
VIAQ IWG Meetings
Notes: 3

## Slide 4
The direction of work
test mode suitable for the interior air emission.
Substances to be measured: Formaldehyde, Acetaldehyde, Benzene, Toluene, Xylene, Ethylbenzene, Styrene, and Acrolein
Working items : 28 total working items
    Closed working items: 15, open issue working items: 13
Development of recommendation document
VIAQ-05-05: VIAQ recommendation document (initial version)
VIAQ Progress Report
Status of Working Items (VIAQ-05-04)
Test mode | Descriptions
Ambient mode | simulates cars parked in the garage overnight.(ambient temp)
Parking mode | simulates cars parked outside in the sunlight(high temp)
Driving mode | simulates air-conditioning conditions right after parking mode(Idling)
Notes: 4

## Slide 5
Closed working item lists
    Protection covers: be taken off one day before the measurement.
    Sampling point: Driver seat (nose position)
Analytics method: ISO 16000-3 (Aldehydes) and ISO 16000-6 (VOCs)
    Definition of new vehicle: new car from serial production, no prototype car
Vehicle age at measurement: 28d ± 5 days after production date
Definition of production date: Sign off date of production line
Vehicle transportation & storage conditions: VIAQ-04-09
Vehicle storage conditions in the plant before transportation : Storage conditions vary in the plant and cannot be controlled.
VIAQ Progress Report
Status of Working Items (VIAQ-05-04)
Notes: 5

## Slide 6
Open working items
Vehicle categories: Category M1, to add N1(Korea), Category 1-1(proposal)
Ambient mode (test temperature): avoid regional options
(Current Status) Ambient test temperature : 25 ℃ vs 23℃
Korea, China, India: 25℃
EC, Russia, OICA: 23℃
Sampling method: Aldehydes is 1.0 L/min and VOCs is 0.2 L/min, 30min
Preconditioning: Storage is 1 day before measurement (soak time)
Parking mode: Sun simulation Radiation of 400W/m² and 4h soak time
Driving mode: Sampling for 30 min with air conditioning
Repeated test: 1 vehicle only once + scientific examination on repeatability
Selection of vehicles: give information on how to select a worst case car
VIAQ Progress Report
Status of Working Items (VIAQ-05-04)
Notes: 6

## Slide 7
Roadmap, Timeline
January 2017 : Submit the VIAQ document as an informal document
June 2017 : Submit the final VIAQ document
2015 2016 2017
1 2 3 4 5 6 7 8 9 10 11 12 1 2 3 4 5 6 7 8 9 10 11 12 1 2 3 4 5 6 7 8 9 10 11 12
171
172
73
75
72
74
71
70
formal
document
Half of working items almost closed
Make a drafting grup
Kick-off
1
2
3
4
6
5
7
9
8
VIAQ recommendation (a new mutual Resolution)
Develop provisions and harmonized test procedures.
WP.29
GRPE
VIAQ
Roadmap
173
VIAQ Madate
Informal
document
Notes: 7

## Slide 8
6th VIAQ IWG Meeting
Paris, 26th – 27st October 2016,
7th VIAQ IWG Meeting
Geneva, Switzerland, January, during 74th GRPE session
Half a day is requested
Next VIAQ IWG Meeting
Next VIAQ IWG Meeting
Notes: 8