## Slide 1: AECS Accident Emergency Call System
Informal document GRSG-111-39
(111th GRSG, 11-14 October 2016,
Agenda item 13)
Submitted by the expert from OICA

## Slide 2
1. Regulatory framework for emergency call systems
Russia: ERA Glonass (Accident Emergency Response system)
Eurasian Custom Union: Russia, Belarus, Kazachstan, Armenia, Kyrgyzstan
2. EU: eCall
3. UNECE: AECS (Accident Emergency call System)
4. Help Net Japan (voluntary emergency call system)

## Slide 3
3
① Vehicle crash happens
② Vehicle sends emergency MSD (Minimum Set of Data) and voice call to 112
③ Mobile Network Operator (MNO) & infrastructure transmit MSD and voice to 112 Public Service Access Point (PSAP, call center)
④ PSAP receives MSD and voice call
⑤ PSAP sends emergency services
3
2
1
5
4
2. Emergency call process

## Slide 4
AECS control unit
GNSS
ANT
AUDIO
BAT
MNO ANT
SP
MIC
INDICATOR
SRS
UNIT,
SENSOR
GNSS
Satellite
SW
3. Basic system lay-out and test requirements
Complexity of the certification process is also determined by
Integration of the emergency call system in the vehicle (one box system, semi integrated or fully integrated)
Supplier responsibility
Can be:
Dedicated power supply
12V starter battery
traction battery
….
MNO antenna can be:
External antenna dedicated to AECS
External antenna for other Vehicle communicaton functions
Antenna integrated in AECD unit
…….
GNSS antenna can be:
External antenna dedicated to AECS
External antenna for navigation system
Antenna integrated in AECD unit
…….
Audio can be:
Dedicated AECS audio speaker/micro
Integrated with vehicle audio
….
Indicator can be:
AECS indicator integrated in AECD
Separate indicator in instrument panel/common place
...
Positioning function can be:
Dedicated AECS positioning module within AECD unit
Take info from vehicle navigation module
...
Trigger detection can be
Dedicated AECS crash sensor
Take signal from vehicle SRS unit
…

## Slide 5
Part I
AECD
Device
Part II
AECD installation
Part III
Vehicle with AECS
1. Current Regulation Proposal (2 procedures to obtain UNECE AECS certification)
4. UN ECE AECS lay-out
2. Additional proposal by OICA for a 1st revision of the AECS Regulation
AECS certificate
AECS certificate
Part I b
AECD
Device
Part II
AECD installation
Part III
Vehicle with AECS
AECS certificate
AECS certificate
Part I a
AECC
Component
AECD certificate
AECC certificate
AECD certificate
Formal Document: ECE-TRANS-WP29-GRSG-2016-19e
Informal Documents:
GRSG-111-06e (AECS secr. Justification)
GRSG-111-07e (AECS secr. Amendment
GRSG-111-13e (Russia amendment for Roll over)
Informal Document:
GRSG-111-15e (OICA proposal for component approval)

## Slide 6
AECD
certificate
AECS
certificate
5. UN ECE AECD details
Part I: AECD (Device)
Part II: AECD (installation)
Par. 7.1: General functioning
Par. 7.3: Positioning
Par. 7.2: EMC
Par. 7.4: Access to PLMN
Par. 7.5: Info & warning signal
Annex 8: Test method
Par. 7.6: Power supply
Par. 7.7: Resistance to impact
Annex 7: Test method
Annex 9: Post-crash perform.
Par. 16.1: Installation requirement
Par. 16.3: Positioning
Par. 16.2: Vehicle impact & trigger
Par. 16.4: AECS Control
Par. 16.5: Info & warning signal
Annex 8: Test method
Par. 16.6: Hands free audio
Par. 16.7: Power supply
Annex 9: Post-crash performance

## Slide 7
AECS
certificate
6. UN ECE AECS details
Part III: AECS (vehicle)
Par. 25.2: EMC
Par. 25.4: Access to PLMN
Par. 25.10: Resistance to impact
Annex 7: Test method
Annex 9: Post-crash perform.
Par. 25.1: General requirements
Par. 25.3: Positioning
Par. 25.5: Vehicle impact & trigger
Par. 25.6: AECS Control
Par. 25.7: Info & warning signal
Annex 8: Test method
Par. 25.8: Hands free audio
Par. 25.9: Power supply
Annex 9: Post-crash performance

## Slide 8
AECD test bench
Component set
High g test
Function check
GNSS
antenna
Manual button
AECD control unit
With intended fixation & part of wire harness
With intended fixation & part of wire harness
w/o fixation
3. Main power supply
If no back-up battery
2. Mobile Network antenna
1. AECD control unit
AECD control unit
7. Resistance to impact (device)
60g (or 65g for EU)
Data transmission check
Position data check
3 possible methods



3. “wired” transmision”
- Mobile network simulator
- Antenna VSWR measurement
or
2. “over the air” transmission
- Mobile network & PSAP simulator
or
1. “Over the air” transmisison
- Real network and PSAP
Wired test can be used for test facility in regions that have MNO frequency restrictions
For EU it can also be performed as a component test by supplier -> OICA has also prepared a AECC (Accident Emergency call Component) certification proposal as a first revision of the AECS Regulation
GRSG discussion

## Slide 9
8. Optional GNSS Positioning test (device or vehicle)
If we use a 3 GNSS compatible GNSS module we can use UNECE Regulation to replace Regional positioning requirement in EU and Russia
EU: GPS + Galileo & EGNOS
Russia : Glonass
UNECE (optional): GPS + Glonass + Galileo & EGNOS optional
GNSS testing
Static Accuracy
Dynamic accuracy
Dynamic shadow accuracy
Cold start
Reacquisition
Sensitivity and calibration



Device or vehicle
Check performance
If not covered by UNECE certification it needs to be covered at national or Regional level

## Slide 10
9. Full scale impact test (vehicle)
Impact test
UNECE R94
UNECE R95
3. “wired” transmision” (not for ERA Glonass)
- Mobile network simulator
- Antenna VSWR measurement
or
2. “Over the air” transmission
- Mobile network simulator & PSAP simulator
Function check
Voice communication
Data transmission
Position check
4 possible methods:
or
1. “Over the air” transmisison
- Real network and PSAP
or
“over the air” transmission
- Mobile network & PSAP simulator
4. Transport vehicle to shielded room (not allowed for ERA Glonass)



OICA is also preparing a post-crash verification method using HMI (as part of 1st revision of AECS Regulation)
Internal Impact testing protocols need to be updated to incorporate post crash emergency call functional tests

## Slide 11
10. In vehicle-self test (device or vehicle)
ECU is in working order (e.g. no internal hardware failure, processor/memory is ready, logic function in expected default state)
External mobile network antenna is connected
Mobile network communication device is in working order (no internal hardware failure, responsive)
External GNSS antenna is connected
GNSS receiver is in working order (no internal hardware failure, output within expected range)
Crash control unit is connected
No communication failures (bus connection failures) of relevant components in this table
SIM is present (this item only applies if a removable SIM is used)
Power source is connected
Power supply state of charge (UNECE only)



Induce malfunction
Check malfunction signal

## Slide 12
11. Audio tests (Vehicle)
Applicable standard
1. Pre-crash audio test (Optional)
Based on ITU P1140 (Hands Free audio systems for emergency call)



Vehicle test
Validation
If UNECE AECS is adopted it can replace the national requirement of a signatory Contracting Party.

## Slide 13
If AECS power supply comes from vehicle power supply (e.g. starter battery)
Demonstrate or calculate
If power supply is part of device (e.g. back-up battery)
- demonstrate
12. Power supply capacity
Requirement
5-60-5 power supply requirement
The emergency call system should have the capability for
5 min talking
60 min stand by
5 min. Talking



Device test
Vehicle

## Slide 14
13. Next Steps
AECS proposal for discussion (and adoption?) at UNECE GRSG-111 in Oct. 2016
UNECE WP.29 in March 2017?
Ratification by United Nations in Sept. 2017?
In parallel discuss
AECC component certification proposal
post-crash verification method using HMI
-> Not clear how further discussion can be done (new IG mandate, ad hoc expert group, … ?)