## Slide 1
SUMMARY OF INITIAL AIMING AND LEVELLING TOLERANCE ISSUE
Poland April 2018
Submitted by the expert from Poland
Informal document GRE-79-23
(79th GRE, 24-27 April 2018, agenda item 6 (b))

## Slide 2
2) TYPE APPROVAL LIMITS ONLY GUARANTEE 20m ROAD ILLUMINATION DISTANCE - WORST CASE (SEE GRE-72-27, GRE-70-41-Rev.1)
3) LACK IN Reg. 48 SPECIFICATION OF AUTOMATIC LEVELLING SYSTEM - E.G. PRECISION AND CHARACTERISTICS (STATIC, DYNAMIC, ETC.)
A) PRESENT STATE OF AIMING AND LEVELLING IN REG. 48 SIGNIFICANTLY INFLUENCE FOR NIGHTTIME TRAFFIC SAFETY
2) 2000 lm FLUX SEPARATION BETWEEN MANUAL AND AUTOMATIC LEVELLING WAS INTRODUCED WHEN HID LIGHT SOURCES WERE BEING INTRODUCED BUT THIS CRITERION IS QUESTIONABLE.
C) ARTIFICIAL FLUX BASED AUTOMATIC LEVELLING OBLIGATION
1) GLARE IS TREATED AS THE MOST IMPORTANT ISSUE
2) VERY SIMPLIFIED LEVELLING REQUIREMENTS IN 1980s NOT TAKING INTO ACCOUNT MOUNTING HEIGHT, ONLY SLIGHTLY MODIFIED IN 1990s
1) AT THE BEGINNING OF UN ECE REGULATION (1950s) MANY YEARS WITHOUT PROVISIONS FOR INITIAL AIM AND LEVELLING TOLERANCE
B) IMPROPER PRESENT „BOX” REQUIREMENTS
1) TYPICAL AUTOMATIC LEVELLING PERFECTLY CONTROL INCLINATION

## Slide 3
D) MISTAKES OF CURRENTLY PRESENTED POSITIONS
1) LOOKING AT GLARE AND IGNORING ROAD ILLUMINATION DISTANCE
BOTH ROAD ILLUMINATION AND GLARE PROTECTION ARE IMPORTANT FOR SAFETY
ROAD USERS COMPLAINTS ARE NOT SUFFICIENT AS JUSTIFICATION
OBJECTIVE SAFETY SHOULD BE BASE FOR DECISION
3) REQUEST TO FIND ALTERNATIVE TO ARBITRAL 2000 lm CRITERION
- NOT POSSIBLE AND NO NEED TO FIND SUCH CRITERION
2) REQUEST FOR AUTOMATIC LEVELLING ONLY
- QUALITY AND PRECISION OF AUTOMATIC SYSTEM IS CRUCIAL
- NOT TECHNOLOGY NEUTRAL
4) CARMAKERS REQUEST TO REQUIRE 1.6% CUT-OFF INCLINATION RANGE FOR MANUFACTURING PURPOSES
- SAFETY AND WORST CASE ARE PRIORITIES FOR TYPE APPROVAL
AUTOMATIC LEVELLING PERFECTLY COMPENSATE MANUFACTURING NON REPEATABILITY AND THERE IS NO JUSTIFICATION TO REQUEST SUCH RANGE AT THE EXPENSE OF SAFETY
- MANUAL LEVELLING MIGHT BE CONDITIONALLY ALLOWED PROVIDING NO NEGATIVE IMPACT FOR ROAD ILLUMINATION AND GLARE

## Slide 4
1) BASED ON CIE 188:2010 STANDARD WHICH IS RELATIVE ONE AND NOT SUITABLE FOR NEW DESIGN. IT WAS INTEND TO COMPARE HEADLAMPS WHICH WERE EARLIER TYPE APPROVED
6) VEHICLE TYPE APPROVED ACCORDING GTB/ OICA MIGHT CAUSE GLARE OR POOR ILLUMINATE THE ROAD
E) GTB/OICA PROPOSAL BASED ON INADEQUATE ASSUMPTIONS
3) THERE ARE NOT THE MINIMUM WORST CASE REQUIREMENTS
4) PROPOSAL BASED ON 50 m RANGE COMBINATION OF SIX ABOVE DIFFERENT HEADLAMPS EACH AT DIFFERENT HEIGHT
2) IT IS BASED ON RESULTS OF SIX ARBITRAL CHOSEN TYPE APPROVED AND GOOD PERFORMING HEADLAMPS BEAM PATTERN (Reg. 112, Reg. 98,) ON REAL CARS MOUNTING HEIGHT Reg. 48
ROAD ILLUMINATION
5) FIXED GLARE WINDOW AT 50 m (CIE 188:2010) AND AVERAGE FLUX IN WINDOW :
- INADEQUATE TO REAL GLARE
- NOT RELEVANT FOR DISTANCE DIFFERENT THAN 50m AND RELATION HEIGHT TO INCLINATION
GLARE

## Slide 5
2) MINIMUM ROAD ILLUMINATION DISTANCE 75m (50m) BASED ON SIMPLE AND OBVIOUS GEOMETRIC CALCULATION
G) POLISH PROPOSAL - STARTING 2011 - TILL NOW
3) SIMILAR GEOMETRIC GLARE CALCULATION AND JUSTIFICATION
1) TRUE PERFORMANCE BASED AND TECHNOLOGY NEUTRAL
5) MANUAL LEVELLING CAN PERFORM ALSO PROPERLY BUT ONLY UNDER SPECIFIC CONDITION (PRECISION, DRIVER AWARENESS AND COOPERATION)
1) THE MAIN ISSUE IS TO GUARANTEE PROPER CUT-OFF INCLINATION FOR ANY LOAD CONDITION
3) SOME AUTOMATIC LEVELLING MAY PERFORM REALLY VERY POOR AND SHOULD NOT BE USED
F) MANUAL OR AUTOMATIC LEVELLING SYSTEM
2) TYPICAL CONTEMPORARY AUTOMATIC LEVELLING SYSTEM CONTROLS CUT-OFF INCLINATION BETTER THAN POSSIBLE TO MEASURE
4) AUTOMATIC LEVELLING IS NOT EXPENSIVE
4) COVER ALL MOUNTING HEIGHTS AND VEHICLES (M, N)

## Slide 6
POLISH PROPOSAL
MINIMUM ROAD
ILLUMINATION DISTANCE
50m
Notes: 6

## Slide 7
Thank you for attention