## Slide 1
Informal document: GRSP-64-37
(64th GRSP, 11 - 14December 2018,
agenda item 9)
Introduction to Revision of UNR17
Proposal Document
ECE/TRANS/WP.29/GRSP/2018/34
Alignment to GTR No. 7 head restraints
December 2018
Submitted by the expert from Japan and
European Commission

## Slide 2
Background
History of alignment to GTR No. 7 head restraints.
At 58th GRSP on December 2015,submitted an informal document for Draft amendment of UNR17(GRSP-58-28Rev.1), That is transpose amendment of GTR7 ph2 (GRSP-58-26) into UNR17 series 08, It was waiting discussion at next GRSP.
However, GTR7 ph2 could not be finalized.
We could not have a discussion for amendment of UNR17.
We submitted an formal document Draft amendment of UNR17 for 64th session of GRSP, that is transpose from amendment of GTR7 ph2 (ECE/TRANS/GRSP/2018/27) into latest document for UNR17(ECE/TRANS/WP.29/2018/142).
※Not yet transpose from GRSP-63-24.
It is the first official document for alignment to GTR No. 7.

## Slide 3
Draft UNR17
Basic concept of transpose from GTR7 to UNR17
While maintaining the current technical standards of UNR 17,
we will add a new standard of GTR 7. The reduced special exception rule of GTR 7 does not apply.
Static
Height
 | Amendment of GTR ph2 | Amendment of UNR17 10series
Height of Head restraint | Not less than 830mm in at least on position…. foot note A contracting party may opt for a lower value in its domestic legislation if it decides that such value in appropriate. | Not less than 830mm in at least on position….
Dynamic performance | Based on a determination by each Contracting Party or regional economic integration organization, either a Hybrid III 50th percentile male dummy or a BioRID II 50th percentile male dummy shall be used to determine compliance. | BioRID II 50th percentile male dummy
No reduced special exception
Use evaluation of cervical
injury value only with BioRIDⅡ

## Slide 4
Draft UNR17
Requirement of draft amendment UNR17 series 10
Change point of UNR17 series 10.
 |  | UNR17 series 08 | amendment UNR17 series 10
Height of head restraint (more than) | Measurement procedure | H-point method | R-point method
 | Highest position(front) | 800㎜ | 830㎜ (outboard)
 | Highest position(other) | 750㎜ | Not applicable
 | Lowest position(front ) | 700㎜ | 720㎜
 | Lowest position(other) |  | 720㎜
 |  |  | 700㎜ (RR CTR)
Back set | Front out board | Not applicable | 45㎜
BioRID2 | All seat if possible to dummy set | Not applicable | Meet injury criteria
※The manufacturer selects either static backset requirement or BioRID 2 requirement

## Slide 5
Draft UNR17
Requirement of draft amendment UNR17 series 10
Change point of UNR17 series 10.
 |  | UNR17 series 08 | amendment UNR17 series 10
Displacement | Application of a 373±7.5Nm moment about the R-point | Not be displaced more than 102㎜ = (b) | Not be displaced more than 102㎜
Displacement and Back set Retention (for backset adjustable) | (a) Application of a 37±0.7Nm initial reference moment. | Not applicable | Not be displaced more than 25㎜
 | (b) Application of a 373±7.5Nm moment about the R-point | Not applicable | Not be displaced more than 102㎜
 | (c)Reduction of moment to 0Nm from(b)and re application of (a) | Not applicable | Return to within 13㎜of initial reference position
If head restraint has adjustable backset , manufacturer possible to choose either requirement.

## Slide 6
Draft UNR17
Requirement of draft amendment UNR17 series 10
Change point of UNR17 series 10.
 |  | UNR17 series 08 | amendment UNR17 series 10
Height retention For adjustable head restraint | Application of initial road 50±1N to 500N after 5 second reduction to 50±1N | Not applicable | Not be displaced more than 25㎜
Non use position | For the front seat | automatically return to the position of use when the seat is occupied. | Not approval for Driver’s seat. for Passenger seat can approve automatically return

## Slide 7
Draft UNR17
Requirement of draft amendment UNR17 series 10
Change point of UNR17 series 10.
 |  | UNR17 series 08 | amendment UNR17 series 10
Non use position | Other seat | provided that such position is clearly recognizable to the occupant as not being included for the use of the head restraint; | automatically return
 |  |  | Not less than rotate 60°
 |  |  | Non comfortable by Gap
 |  |  | Non comfortable by big difference of torso
 |  |  | Information label

## Slide 8
Draft UNR17
Outlook / Recommendation
GTR7 ph2 is the finalization stage now.
In the meantime, the IWG of GTR7ph2 would welcome comments on the content of document ECE/TRANS/WP.29/GRSP/2018/34 so that it may consider them while preparing the final proposal.

## Slide 9
Thank you for your attention!
Head restraint working group passive safety subcommittee in JASIC
Japan automobile standards internationalization center