## Slide 1
Transmitted by the Chair and Secretary of VIAQ
Chair: Andrey KOZLOV, Russian Federation
Co-Chair: Jongsoon LIM, The Republic of Korea
Secretary: Mark POLSTER, Ford
Status Report of the
VIAQ (Vehicle Interior Air Quality)
Informal Working Group
GENEVA, May 21-24th 2019
Informal document GRPE-79-18
79th GRPE, 21-24 May 2019
Agenda item 12

## Slide 2
Background
During 173rd WP.29 session in Geneva (14-17 November 2017) Proposal for a new Mutual Resolution (M.R.3) for of the 1958 and the 1998 Agreements concerning Vehicle Interior Air Quality (VIAQ) was adopted (ECE/TRANS/WP.29/2017/136).
Final text of Mutual Resolution M.R.3 was published at UNECE site on 1 of November 2018 as the document ECE/TRANS/WP.29/1143
Notes: 2

## Slide 3
Terms of reference
ToR for the Second Stage
Identify and collect the information and research data on interior air quality and its relevance for vehicles, taking into account the activities being carried out by various governments, and non-governmental organizations.
Identify and understand the current regulatory requirements with respect to vehicle interior air quality in different markets.
Identify, review and assess existing test procedures suitable for the measurement of harmful substance into the vehicle cabin (including test modes, sample collection methods and analysis methods, etc.)
Develop provisions and test procedures in a recommendation by including Part 3 in the Mutual Resolution No. 3.
Notes: 3

## Slide 4
Timeline
ToR for the Second Stage
January 2020: Submit the draft document to GRPE
June 2020: Adoption of the draft document by GRPE
November 2020: Adoption of the draft document by WP.29
2018 2019 2020
1 2 3 4 5 6 7 8 9 10 11 12 1 2 3 4 5 6 7 8 9 10 11 12 1 2 3 4 5 6 7 8 9 10 11 12
180
181
79
81
78
80
77
76
formal
document
Half of working items almost closed
Make a drafting grup
11
12
Develop provisions and harmonized test procedures.
VIAQ recommendation (a new part of M.R.3)
WP.29
GRPE
VIAQ
182
VIAQ Madate
Informal
document
13
14
15
16
17
18
19
20
Notes: 4

## Slide 5
16th VIAQ IWG Meeting
  Paris, France, May 14-15th 2019
  Two days
VIAQ IWG Meetings since the last GRPE sessions
Notes: 5

## Slide 6
Working Items
Vehicle Category
Test Vehicle age/millage
Substances to be Measured*
Meteorological Conditions
General Test Conditions
Test Modes
HVAC Modes*
Test Procedure*
Measurement Methods
Sampling Points
Sampling Method
Test Protocol
* Need clarification of some particular aspects
Notes: 6

## Slide 7
Category 1-1
1. Vehicle Category
Agreed Item
Working Items
Notes: 7

## Slide 8
New cars from series production
Millage
3 000 -15 000 km
2. Test Vehicle age/millage
Working Items
Agreed Item
Notes: 8

## Slide 9
Formaldehyde СН2О Nitrogen dioxide NO2 Nitrogen oxide NO Carbon monoxide СО Saturated hydrocarbons (С2Н6…С7Н16) Methane CH4
Carbon monoxide СО Nitrogen oxide NO
Nitrogen dioxide NO2
3. Substances to be Measured
Russian Standard
Working Items
Agreed substances
Carbon monoxide СО
Nitrogen oxide NO Nitrogen dioxide NO2
Korea
Formaldehyde СН2О
Particulate matter (PM)
For discussion
(see VIAQ-13-04 and VIAQ-14-04)
Notes: 9

## Slide 10
4. Meteorological Conditions
Working Items
ambient air temperature:
from -7°C to +30°C
relative humidity:
from 30% to 90%
atmospheric pressure
from 85 to 110 kPa
Agreed Item
Notes: 10

## Slide 11
5. General Test Conditions
Working Items
Test facility for idle test is an open parking zone.
Test road for constant speed test is a paved road with the slope up to 6.0%.
For the purpose of idle test it is possible to use natural wind (if within the specification) or air blower to provide uniform air flow along the tested vehicle with a velocity of 2±1 m/s.
During the tests contamination from outside sources has to be prevented. Therefore background measurements of the analytical substances have to be done before and after the test and in constant speed mode a distances to emission sources has to be not less than 100 m.
General inspection should be checked before testing.
Windows, doors and ventilation hatches should be closed.
HVAC outside flaps have to be closed.
Agreed Item
Notes: 11

## Slide 12
6. Test Modes
Working Items
1. Idling Test
2. Constant Speed Test
  Movement at constant speed 50 km/h
  Movement at constant speed 130 km/h (options: 90 or 110 km/h)
Agreed Item
  Movement at constant speed 130 km/h (options: 90 or 110 km/h)
Notes: 12

## Slide 13
7.HVAC Modes / 8.Test Procedure
Working Items
Idle test
wind direction
1.0 m
0.5 m
0.5 m
3
2
1
0.5 m
1 - Anemometer (constantly monitor center location); 2,3 - Anemometers (side location)
Test conditions:
wind velocity 2.0±1 m/s
velocity difference between anemometers 1, 2 and 3 not more than 15%
HVAC mode:
  recirculation: ON
  air conditioner: OFF
  ventilator speed: MAXIMAL
  outside air flaps: closed
  temperature setting: manual and coolest level
  dashboard vent: all open and horizontal
  rear vents: closed
It is acceptable to use air blower to simulate air movement around tested vehicle
Notes: 13

## Slide 14
7.HVAC Modes / 8.Test Procedure
Working Items
Insure the wind speed is equal to 2±1 m/s in case of testing at natural air movement.
Park the vehicle in a position so the wind direction achieves a linear speed of air perpendicular to the rear of the test vehicle.
Locate the sensors to the center point behind the test vehicle to measure wind speed, temperature and humidity.
Verify the uniformity of the wind to insure it is constant across the vehicle within the airflow tolerance and perpendicular to the rear of the vehicle.
Start the engine and warm-up vehicle by driving for a minimum 15 minutes.
After warm-up, park the vehicle by backing into the previous position. Set the vehicle’s climate system to air conditioner: OFF; recirculation: ON; outside air flaps: closed: temperature: manual and coolest level; fan: highest level; dashboard vent: all open and horizontal, and rear vents: closed.
With the engine off, ventilate vehicle for 5 minutes with all doors and windows open. Then close the doors and windows. During sampling, no people are inside the test vehicle.
With the engine off measure the background pollutant concentrations.
Open the door, start the engine, confirm the climate system settings, exit and close the door. This operation should take about one minute. Sample air from a location between the front seats for 10 minutes.
Take another background measurement according to chapter 8.
Vehicle idle test is complete.
Idle test
Notes: 14

## Slide 15
7.HVAC Modes / 8.Test Procedure
Working Items
Constant speed test
Speed modes:
  50 km/h (city traffic)
  130 km/h (highway)
HVAC mode:
  air conditioner: OFF
  recirculation: ON
  ventilator speed: MAXIMAL
  outside air flaps: closed
  temperature setting: 20±2oC
  dashboard vent: all open and horizontal
  rear vents: closed
  air conditioner: OFF (option is ON)
  130 km/h (options: 90 or 110 km/h)
Notes: 15

## Slide 16
7.HVAC Modes / 8.Test Procedure
Working Items
Start the engine and warm-up vehicle by driving for a minimum 15 minutes.
After warm-up, park the vehicle and set the vehicle’s climate system to air conditioner: OFF; recirculation: ON; outside air flaps: closed; temperature: 20±2oC; fan: highest level; dashboard vent: all open and horizontal, and rear seat vents: closed.
With the engine off, ventilate vehicle for 5 minutes with all doors and windows open. Then close the doors and windows.
With the engine off measure the background pollutant concentrations.
Start the engine, confirm the climate system settings. Start driving and accelerate smoothly to a speed of 50 km/h. Measure the vehicle interior pollutant concentration level. Sample air from a location between the front seats for 10 minutes.
Repeat measurement in accordance with item 5 at a speed of 130 km/h.
Take another background measurement according to chapter 4.
Stop all measurements, park the vehicle and switch engine off.
Vehicle constant speed test is complete.
Constant speed test
Notes: 16

## Slide 17
9. Measurement Methods
Working Items
Substances | Proposed measuring methods | Type of analysis
CH2O | High performance liquid chromatography (HPLC) UV detection | 1) Off-line analysis at the laboratory after preliminary air sampling to the cartridges
 | 2) Gas chromatography (GC) with nitrogen phosphorus detection (NPD), or mass spectrometer (MS) and capillary or packed columns | 2) Off-line analysis at the laboratory after preliminary air sampling to the cartridges
 | 3) Photo-electric colorimetric method | 3) On-line (express) analysis
NO, NO2 | 1) Chemiluminescence (CLD) | 1) On-line (express) analysis or stationary analysis at the laboratory after preliminary air sampling to the sealed bags
 | 2) High-sensitivity electrochemical detection (ECD) | 2) On-line (express) analysis
CO | 1) Infrared photoacoustic spectroscopy | 1) On-line (express) analysis
 | 2) Electrochemical detection (ECD) | 2) On-line (express) analysis
PM2,5 PM10 | Light-scattering laser photometer need additional discussion | 1) On-line (express) analysis
Notes: 17

## Slide 18
10. Sampling Points / 11.Sampling Method
Working Items
The sampling point is between headrests of front seats
The sampling method is aspiration
Agreed Item
Notes: 18

## Slide 19
12. Test Protocol
Working Items
The data exchange file shall be constructed as follows. Pollutant concentrations as well as any other relevant parameters shall be reported and exchanged as a csv-formatted data file. Parameter values shall be separated by a comma, ASCII-Code #h2C. The decimal marker of numerical values shall be a point, ASCII-Code #h2E. Lines shall be terminated by carriage return, ASCII-Code #h0D. No thousands separators shall be used.
Headers of the Reporting and Data Exchange File are in the table (for example)
Line # | Parameter | Basic Data Type [A=Alpha or N=Numeric (max length, fractional digits)] | Data Type [Enumeration String, Decimal, Integer] | Total Digits | Fractional Digits | Minimum Value | Maximum Value | Allowed Values for: Enumeration or Description or Units
1 | Process Code | N(2) | Integer |  |  | 0 | 99 | Version of Test Report. 1st dataset is N=0, highest value is the latest correction of existing dataset
14 | Factory Name | A(50) | String |  |  |  |  | Place of Manufacturer
15 | Vehicle Identification Number | A(17) | String |  |  |  |  | 17-character vehicle identification number (VIN)
31 | Background – Carbon Monoxide | N(4,1) | Decimal | 5 | 1 | 0.0 | 9999.9 | CAS#: 201230-82-2 [mg/m^3]
32 | Background – Nitrogen Monoxide | N(4,1) | Decimal | 5 | 1 | 0.0 | 9999.9 | CAS#: 10102-43-9 [µg/m^3]
33 | Background – Nitrogen Dioxide | N(4,1) | Decimal | 5 | 1 | 0.0 | 9999.9 | CAS#: 10102-44-0 [µg/m^3]
Notes: 19

## Slide 20
Items which need additional clarification
Substances to be Measured
  Formaldehyde СН2О
  Particulate matter (PM2.5 and PM10)
Constant speed test
  Speed 130 km/h (options: 90 or 110 km/h)
  Air conditioner: OFF (option is ON)
Working Items
Notes: 20

## Slide 21
Developed and edited during 16th meeting two documents:
Update of part I of Mutual Resolution No. 3 (VIAQ-16-06)
Draft of part III of Mutual Resolution No. 3 (VIAQ-16-08)
as parts of Revision 2 of Mutual Resolution (M.R.3) on Vehicle Interior Air Quality
Revision 2 of M.R.3
Notes: 21

## Slide 22
Next VIAQ IWG Meeting
17th VIAQ IWG Meeting (TBD)
  Munich, Germany, November 6-7th 2019
  Two days
18th VIAQ IWG Meeting (TBD)
  • Geneva, Switzerland, January 8th 2020
  • Half a day
Notes: 22