## Slide 1: Transposition of GTR15 (WLTP) and GTR19 (Evap) into UN Regulations Update for GRPE from WLTP Transposition Task Force June 2020
Informal document GRPE-80-37
80th GRPE, 14-17 January 2020
Agenda item 3(a)

## Slide 2: Background
TASK = Transpose GTR15 WLTP and GTR19 EVAP into a new ‘UNR WLTP’ regulation
Level 2 to contain most stringent requirements from across all regions
  Subject to full mutual recognition: TA shall be accepted by all CPs
Regional levels (Level 1A, 1B etc. ) to contain regional requirements
  Optional acceptance by other CPs
  EU and Japan are the two CPs to be represented
UNR WLTP to be ‘accompanied by’ a UNR83 08 series that covers all the requirements of UNR83 07 series not covered by new UNR WLTP (e.g. Low temperature test etc.)
  Original scheme was to introduce at same time as UNR WLTP. It will now be introduced at the same time as UNR RDE, i.e. one GRPE later
  As and when GTR15 and UNR WLTP add new tests (e.g. Type 6 test) ‘UNR 83 08 series’ will ‘shrink’ in content.
  EU would be a CP to UNR No. 83 and UNR WLTP. Japan would be a CP to just UNR WLTP

## Slide 3: Schematic of proposed transposition route
* Where other tests refer to the Type I test (NEDC) it will be necessary to say (where appropriate) that this should be seen to be the WLTP Type 1 test (over a certain transition period in some cases)
UNR WLTP
Level 1a (Europe) – including Type 1, 4 and 5 tests
UNR 83 08 series
Shall demonstrate compliance with Level 1A of UNR WLTP
Type I test
Type III test – modified for ‘WLTP world’ *
Type V test – modified for ‘WLTP world’ *
Type VI test – modified for ‘WLTP world’ *
OBD, ISC
Level 2 most stringent – including Type 1, Type 4 and Type 5 tests
Level 1b (Japan) – including Type 1, 4 and 5 tests
+
Type II test – modified for ‘WLTP world’*
Type IV test

## Slide 4: Post-79th GRPE Update
  Intensive activity of the various WLTP IWG Task Forces contributing to the content and drafting of the UNR, in particular those for Conformity of Production, Durability, Sub-Group EV, OBD and the Transposition Task Force
  Working Documents submitted for the 80th GRPE
    00 series: GRPE-20-03
    01 series: GRPE-20-04
  Further work on various elements of the UNR has required the development of Informal Documents to amend these two Working Documents
    These have been submitted to the 80th GRPE
  Decision taken to postpone UNR83 08 by one GRPE session
    The ISC requirements will need to align with UNR RDE

## Slide 10: Modifications in Informal Documents
  The Working Documents included several sections/paragraphs in square brackets – these needed to be considered for their inclusion in UNR (or not)
  Key changes in the Informal Documents relate to the following topics (inter-alia):
    Updates for Conformity of Production for Type 1 and Type 4 tests
    Updates for Type 5 Durability test
    Introduction of changes from the Gear Shift Task Force
    Addition of requirements for fuel efficiency
    Amendments to the Type 1 test post-processing tables
    Addition of requirements for OVC-FCHVs (into Level 1A only)
    Inclusion of revised OBD requirements to align with ‘WLTP world’

## Slide 11: Next Steps
UNR WLTP development group to have a well deserved break from UNR!
Development of the 08 Series for UNR 83 – alongside the UNR RDE
  Working Document for 81st GRPE
Align GTR15 with UNR WLTP (where appropriate) via a new GTR No. 15 Amendment 6
  Working Document for 81st GRPE

## Slide 12
Thank you for your attention
Questions?
Contact information
Rob Gardner, TRL Ltd on behalf of the European Commission (Task Force Leader)
rgardner@trl.co.uk