Informal document No. 8

(48th GRRF, 11-13 September 2000,

Agenda Item 2)

Method of analysis for Japanese accidents and data

#### Submitted by Japan

Since it was decided at the special GRRF held in December of 1999 that data on Rollover accidents shall be presented, Japan’s outlook and accident data are submitted herein.

Outline on collection of data on Rollover accidents

Data on Rollover accidents

| Item | 1 | 2 | 3 |
| --- | --- | --- | --- |
| Facts pertaining to accident conditions | Rollover configuration | after passing | left curving | left curving |
|  | Vehicle speed(km/h) | 60 | 51 | 40 |
|  | Road radius | straight |  |  |
|  | Radius of tire marks on road |  |  |  |
|  | Brake application method |  |  |  |
|  | Length of tire marks on road |  |  |  |
| Facts pertaining to vehicle in accident | Vehicle specification | Vehicle model | U-FE437F | W-CK610BNT TF1591 | P-FP410DR TF1591 |
|  |  | Rear body configuration |  |  |  |
|  | Vehicle condition | Gross weight at time of accident(kg) | 2000(loading weight) | 9987(loading weight) | 13000 (loading weight) |
|  |  | Loading position |  |  |  |
|  |  | Height of gravity center at the time of accidents |  |  |  |
| Facts pertaining to the road surface | Road surface condition | Pavement condition and weather | freezing snow | wet rain | dry fine |
|  | Road surface structure | Road radius |  |  |  |
|  |  | road inclination | forward incline | even | down | down |
|  |  |  | lateral incline | track |  |  |
| Facts pertaining to driving operations and managements | Presence/absence of excessive load | absence | absence | absence |
|  | vehicle maintenance | no trouble | no toruble | no trouble |
|  | running management, etc |  |  |  |
|  | Steering wheel operation | not good | over speeded | over speeded |
|  | Presence/absence of brake operation |  |  |  |
|  | Driving career (years) | 17 | 5.3 | 30.3 |
| Social costs incurred by rollover accidents | Traffic snarls |  |  |  |
|  | Restorations and other infrastructure costs |  |  |  |
|  | Accident victims and other human costs | minor injury 1 | serious injury 1 | serious injury 1 |

Data on Rollover accidents

| Item | 4 | 5 | 6 |
| --- | --- | --- | --- |
| Facts pertaining to accident conditions | Rollover configuration | left curving | left curving | left curving |
|  | Vehicle speed(km/h) | 55 | 50 | 40 |
|  | Road radius |  |  |  |
|  | Radius of tire marks on road |  |  |  |
|  | Brake application method |  |  |  |
|  | Length of tire marks on road |  |  |  |
| Facts pertaining to vehicle in accident | Vehicle specification | Vehicle model | KC-FP410DR HT2552 | KC-SS3VJCA P239D | W-CK620BNT TF1591 |
|  |  | Rear body configuration |  |  |  |
|  | Vehicle condition | Gross weight at time of accident(kg) | 20000 (loading weight) | 20010 (loading weight) | 27000 (loading weight) |
|  |  | Loading position |  |  |  |
|  |  | Height of gravity center at the time of accidents |  |  |  |
| Facts pertaining to the road surface | Road surface condition | Pavement condition and weather | dry cloudy | wet cloudy | dry fine |
|  | Road surface structure | Road radius |  |  |  |
|  |  | road inclination | forward incline | up | even | down |
|  |  |  | lateral incline |  |  |  |
| Facts pertaining to driving operations and managements | Presence/absence of excessive load | absence | presence (max.17750kg) | presence (max.19250kg) |
|  | vehicle maintenance | no trouble | no trouble | no trouble |
|  | running management, etc |  |  |  |
|  | Steering wheel operation | over speeded | over speeded | not good |
|  | Presence/absence of brake operation |  |  |  |
|  | Driving career (years) | 2 | 7.4 | 0.2 |
| Social costs incurred by rollover accidents | Traffic snarls |  |  |  |
|  | Restorations and other infrastructure costs |  |  |  |
|  | Accident victims and other human costs | minor injury 1 | serious injury 1 minor injury 1 | minor injury 1 |

Data on Rollover accidents

| Item | 7 | 8 | 9 |
| --- | --- | --- | --- |
| Facts pertaining to accident conditions | Rollover configuration | left curving | left curving (passing) | gale |
|  | Vehicle speed(km/h) | 60 | 50 |  |
|  | Road radius |  |  |  |
|  | Radius of tire marks on road |  |  |  |
|  | Brake application method |  |  |  |
|  | Length of tire marks on road |  |  |  |
| Facts pertaining to vehicle in accident | Vehicle specification | Vehicle model | KC-SS3VJCA TF28H8C2 conv | KC-CK551BNT CT220D | U-FK516S |
|  |  | Rear body configuration |  |  |  |
|  | Vehicle condition | Gross weight at time of accident(kg) | 20000 (loading weight) | 17000 (loading weight) | 0 (loading weight) |
|  |  | Loading position |  |  |  |
|  |  | Height of gravity center at the time of accidents |  |  |  |
| Facts pertaining to the road surface | Road surface condition | Pavement condition and weather | wet rainy | dry fine | wet cloudy |
|  | Road surface structure | Road radius |  |  |  |
|  |  | road inclination | forward incline | up | up | even |
|  |  |  | lateral incline |  |  |  |
| Facts pertaining to driving operations and managements | Presence/absence of excessive load | absence | absence | absence |
|  | vehicle maintenance | no trouble | no trouble | no trouble |
|  | running management, etc |  |  |  |
|  | Steering wheel operation | over speeded |  |  |
|  | Presence/absence of brake operation |  |  |  |
|  | Driving career (years) | 7 | 21.5 | 2.9 |
| Social costs incurred by side turn accidents | Traffic snarls |  |  |  |
|  | Restorations and other infrastructure costs |  |  |  |
|  | Accident victims and other human costs |  |  |  |

Data on Rollover accidents

| Item | 10 | 11 | 12 |
| --- | --- | --- | --- |
| Facts pertaining to accident conditions | Rollover configuration | left curving | left curving | curving |
|  | Vehicle speed(km/h) | 60 | 28 |  |
|  | Road radius |  |  |  |
|  | Radius of tire marks on road |  |  |  |
|  | Brake application method |  |  |  |
|  | Length of tire marks on road |  |  |  |
| Facts pertaining to vehicle in accident | Vehicle specification | Vehicle model | P-FV415JR TF242-1 | P-RR170BA | U-CM88KE |
|  |  | Rear body configuration |  |  |  |
|  | Vehicle condition | Gross weight at time of accident(kg) | 30400 (loading weight) |  | 2500 (loading weight) |
|  |  | Loading position |  |  |  |
|  |  | Height of gravity center at the time of accidents |  |  |  |
| Facts pertaining to the road surface | Road surface condition | Pavement condition and weather | wet rainy | dry fine | wet rainy |
|  | Road surface structure | Road radius |  |  |  |
|  |  | road inclination | forward incline | down | up | down |
|  |  |  | lateral incline |  |  |  |
| Facts pertaining to driving operations and managements | Presence/absence of excessive load | presence (max.30400kg) | absence | absence |
|  | vehicle maintenance | no torouble | no trouble | no trouble |
|  | running management, etc |  |  |  |
|  | Steering wheel operation | over speeded | over speeded | careless |
|  | Presence/absence of brake operation |  |  |  |
|  | Driving career (years) | 7.9 | 0.2 | 5.5 |
| Social costs incurred by rollover accidents | Traffic snarls |  |  |  |
|  | Restorations and other infrastructure costs |  |  |  |
|  | Accident victims and other human costs | death 1 | serious injury 1 minor injury 16 | death 1 |

Data on Rollover accidents

| Item | 13 | 14 | 15 |
| --- | --- | --- | --- |
| Facts pertaining to accident conditions | Rollover configuration | left curving | right turning | left curving |
|  | Vehicle speed(km/h) |  |  | 100 |
|  | Road radius |  |  |  |
|  | Radius of tire marks on road |  |  |  |
|  | Brake application method |  |  |  |
|  | Length of tire marks on road |  |  |  |
| Facts pertaining to vehicle in accident | Vehicle specification | Vehicle model | W-CR610BAT ST20SA conv | KC-CK551BHT FKC220A | KC-SS1FJCA TF40337 |
|  |  | Rear body configuration |  |  |  |
|  | Vehicle condition | Gross weight at time of accident(kg) | 15000 (loading weight) | 20000 (loading weight) | 37030 (loading weight) |
|  |  | Loading position |  |  |  |
|  |  | Height of gravity center at the time of accidents |  |  |  |
| Facts pertaining to the road surface | Road surface condition | Pavement condition and weather | dry cloudy | wet rainy | dry fine |
|  | Road surface structure | Road radius |  |  |  |
|  |  | road inclination | forward incline | even | down | down |
|  |  |  | lateral incline |  |  |  |
| Facts pertaining to driving operations and managements | Presence/absence of excessive load | absence | absence | absence |
|  | vehicle maintenance | no trouble | no trouble | no trouble |
|  | running management, etc |  |  |  |
|  | Steering wheel operation |  |  | over speeded |
|  | Presence/absence of brake operation |  |  |  |
|  | Driving career (years) |  |  |  |
| Social costs incurred by rollover accidents | Traffic snarls |  |  |  |
|  | Restorations and other infrastructure costs |  |  |  |
|  | Accident victims and other human costs | death 1 | death 1 | death 1 |

# Text boxes

Accident data collection

・Facts pertaining to accident conditions

Rollover configuration, Vehicle speed, Road radius, Radius of tire marks on road, Brake application method, Length of tire marks on road

・Facts pertaining to vehicle in accident

vehicle specification：vehicle model、rear body configuration

Vehicle condition：Gross weight, loading position, height of gravity center at the time of accidents

・Facts pertaining to the road surface

Road surface condition：Pavement condition and weather

Road surface structure：Road radius, road inclination

(forward incline, lateral incline)

・Facts pertaining to driving operations and managements

Presence/absence of excessive load, vehicle maintenance, running management, etc. Steering wheel operation, presence/absence of brake operation, driving career

・Social costs incurred by side turn accidents

Traffic snarls, restorations and other infrastructure costs, accident victims and other human costs

Vehicle lateral acceleration at time of accident

Adjust for the test method

Establishment of lateral acceleration standard value

Investigation of the costs/effects

Investigation of appropriate improvement measures

Calculation of effect

Calculation of costs

Revision of established acceleration standard value

Environmental factors

Human factors

Vehicle development and production costs

Revision of established acceleration standard value

Estimate the effect of accident reduction