AMENDMENTS TO DOCUMENTS TRANS/WP.29/GRSG/1999/20 AND ADD.1

Transmitted by the expert from Sweden

# A.	Document TRANS/WP.29/GRSG/1999/20

## Annex 3

Insert new figures 12a to 14, to read:

“

Figure 12a Pictogram for wheelchair users

Figure 12b: Pictogram for passengers with reduced mobility

other than wheelchair users

Overall length,	l:		1200 mm

Overall width,	b:		 700 mm

Overall height,	h:		1090 mm

Note: A wheelchair user seated in the wheelchair adds 50 mm to the overall length and makes a height of 1,350 mm above the ground.

Figure 13 Wheelchair type

Figure 14: Minimum clear space for the wheelchair user

at the wheelchair space”

# B.	Document TRANS/WP.29/GRSG/1999/20/Add.1

Annex 7,

Paragraph 3.4.1., amend to read:

“ ....... to the wheelchair space or to the priority seat.”

Paragraph 3.5., amend to read:

“ .... not exceed 8 per cent.  Such sloping areas shall be provided with a non-slip surface.”

Paragraph 3.6.2., amend to read:

“ ... the provisions of paragraph 3.11.2. (a kneeling system), of this annex; this shall be in combination with the provisions of paragraph 3.11.3. (a lift) or 3.11.4. (a ramp) of this annex.”

Paragraph 3.8.1.1., amend to read:

“ ...  are not required to be fitted with any kind ... ”

Paragraph 3.8.1.2., amend to read:

“ ....

This restraint system and its anchorages shall be ....”

Note: These amendments complement those adopted during the seventy-ninth session.

__________________