# Corrigendum to draft Regulation on the protection of

# M1 and N1 vehicles against unauthorized use

Paragraph 8.1.1., amend to read:

“ ..... normal driving away of a vehicle under its own power (prevention of unauthorized use).”

Paragraph 8.1.4., amend to read:

“ ..... cannot be driven normally under its own power.”

Insert a new paragraph 8.2.11., to read:

“8.2.11.		It shall not be possible for an immobilizer to operate in such a manner as to apply the brakes of the vehicle.”