## Slide 1: Systems to Prevent Small Children from Being Left Unattended in Vehicles
Informal document GRSP-69-16
(69th GRSP, 17- 21 May 2021,
agenda item 23(f) )
Ministry of Sustainable Infrastructure and Mobility

## Slide 2: Legal Framework
Law No. 117 of 1st October 2018 - concerning use of systems to prevent children from being left unattended in vehicle involuntary – amended the Italian National Highway Code (art. 172).
Ministerial Decree No. 122 of 2nd October 2019 concerning administrative and technical rule for systems to prevent children from being left unattended in vehicle involuntary

## Slide 3: Main Action
Mandatory from 7 November 2019, to have a Child Reminder Systems when a children under 4 years old is transported
Fiscal incentives are issued for a quick implementation
An awareness campaigns is carried out.

## Slide 4: Ministerial Decree No. 122 (1/4)
The Ministerial Decree identifies three different type of system to prevent children from being left unattended in vehicle involuntary:
System originally integrated in vehicles
System originally integrated in child restraint systems itself
Separate system
For each type of system, the functionality requirements and the applicable technical standards are established.

## Slide 5: Ministerial Decree No. 122 (2/4)
Functional requirements for all system (1/2)
The system shall signal to the driver of the vehicle that a child is left on the vehicle on which he is transported by activating one of the signals referred to letter d);
The system shall activate automatically at each use, without further action by the driver;
The system shall give a confirmation signal to the driver at the moment of activation;

## Slide 6: Ministerial Decree No. 122 (3/4)
Functional requirements for all system (2/2)
In case of the system detects that an alarm signal is needed, the signal shall obtain the driver's attention promptly by a visual and acoustic or visual and haptic signals, perceptible inside or outside the vehicle
The system shall activate the communication system indicated in letter g);
If powered by a battery, the system shall signal to the driver the low levels of remaining charge;
The system may be equipped with an automatic communication system for sending messages or calls via wireless mobile communication networks.

## Slide 7: Ministerial Decree No. 122 (4/4)
Technical requirements for separate system
The system must be based on electronic systems with usage logics or which use special sensors;
When interacting with the vehicle or with a child restraint system, the system shall not effect the type approval of vehicle or child restraint system

## Slide 8: Examples of best-selling products

## Slide 9: Device on Safety Belt

## Slide 10: Cushion under Baby

## Slide 11: Reference
https://www.mit.gov.it/comunicazione/news/seggiolini-antiabbandono
https://www.gazzettaufficiale.it/eli/id/2019/10/23/19G00130/sg
https://www.piuvenduti.it/dispositivi-anti-abbandono/

## Slide 12: Thanks for Your Attention