## Slide 1
UN R13 and Electro Mechanical Brakes
Submitted by the expert from the European Association of Automotive Suppliers CLEPA | Informal document GRVA-10-23 10th GRVA, 25-28 May 2021 agenda item 8(b)

## Slide 2
ECE-R13 and Electro Mechanical Brakes (EMB) Overview of changes made to Informal Document GRVA-09-05
With respect to GRVA-09-05, changes were made in the following paragraphs:
- 2.31.
- 2.51.
- Correction in Justification of paragraph 5.1.4.5.1.
- PTI paragraph 5.1.4.5.3. (with new Justification)
- 5.1.4.6.2.1.
- 5.1.4.6.2.1 & 5.1.4.6.2.2 & 5.1.4.6.2.3 (word “wheel” deleted)
- Proposal for deletion of paragraph 1.2.11. of Annex 4 withdrawn
- Note, that paragraph 2.4.1 of Annex 7, Part D is still under discussion

## Slide 3
Combustion engine
compressor
4 circuits protection valve
Air tank (FA)
600V
compressor
4 circuits protection valve
Air tank (FA)
Wheels
Energy transmission
Motor/ gene-rator
Energy transmission
Diesel engine
BEV
EBS
Vehicles with pneumatic braking do have an ‘energy source’
Energy source
Energy source
(Layout Examples)
Explanation to Paragraph 2.51
2.49. "Energy source" means a device that both generates and provides energy required for the braking system.

## Slide 4
Combustion engine
Electrical Storage Device (FA)
600V
Wheels
Motor/ gene-rator
Electrical Storage Device (FA)
Diesel engine
BEV
EMB
Circuits insulation
Circuits insulation
24V
Generator
M
M
Electrical Supply Device
Vehicles with an EMB can have an ‘energy source’,
But it is called an ‘electrical supply device’
Energy transmission
Energy transmission
(Layout Examples)
24V
DC/DC
2.51. "Electrical supply device" means a device (e.g. battery, REESS, DC/DC converter, generator, fuel-cell or a combination of those components) that supplies electrical energy to the braking system's electrical energy storage device(s).
Explanation to Paragraph 2.51

## Slide 5
Combustion engine
Electrical Storage Device (FA)
600V
Wheels
Motor/ gene-rator
Electrical Storage Device (FA)
Diesel engine
BEV
Circuits insulation
Circuits insulation
M
M
EMB
Generator
Energy transmission
Energy transmission
Electrical Supply Device
(Layout Examples)
Vehicles with an EMB can have an ‘energy source’,
But it is called an ‘electrical supply device’
DC/DC
Explanation to Paragraph 2.51
2.51. "Electrical supply device" means a device (e.g. battery, REESS, DC/DC converter, generator, fuel-cell or a combination of those components) that supplies electrical energy to the braking system's electrical energy storage device(s).

## Slide 6
PTI update

## Slide 7
PTI update

## Slide 8
PTI update