## Slide 1
Page 1
This presentation supports the draft proposal for the
new 01 series of amendments to UN Regulation No. 150
(GRE/2021/15)
GRE IWG „Simplification of Lighting and Light-Signalling Regulations“
Reg. 150 Stage II, Step 1 – Summary
GRE
IWG
SLR
Informal document GRE-85-05
85th GRE, 26-29 October 2021
Agenda item 4 (d)

## Slide 2
GRE
IWG
SLR
Page 2
Update of the definitions Correction of the Photometric Definitions
"Coefficient of luminous intensity RI" means the quotient of the luminous intensity I reflected by the retro-reflective device in the direction considered, divided by the normal illumination of the retro-reflecting device for given angles of illumination, divergence and rotation.
"Specific coefficient of retro-reflection (symbol RA)" means the quotient of the coefficient of luminous intensity R of a plane retro-reflecting surface and its area A
The coefficient of retro-reflection RA is expressed in candelas per m2 per lx (cd∙m-2∙lx-1)
“Specific coefficient of retro-reflection (symbol R')" means the quotient of the coefficient of luminous intensity R of a plane retro-reflecting surface and its area A
In the current version of Reg 150 (based on former Reg 3) – no definition of the CIL value is given
NEW
NOTE 1 RI is often referred to as CIL. The unit is cd/lx.
R´  RA
Old definition of R´
Reference document:
CIE Publication 54.2:2001 ”Retroreflection: Definition and measurement”

## Slide 3
"Luminance factor (symbol RF)" means the ratio of the luminance of the body to the luminance of a perfect diffuser under identical conditions of illumination and observation;
Luminance factor
(symbol ß) - means the ratio of the luminance of the body to the luminance of a perfect diffuser under identical conditions of illumination and observation;
(symbol β)  (symbol RF)
All definitions for angles are Greek symbols (a, b, …) – to prevent mix-ups.
Definition of the angles for the measuring geometry setup
In Reg. 150 there is a mix of the definitions for the observation angles.
E.g. βV , βH or V , H or β1 , β2
Depending on Regulation 3 or 70, 104, …
"Observation angle (symbol α)" means the angle between the illumination axis and the observation axis. The observation angle is always positive and, in the case of retro-reflection, is restricted to small angles;
"Entrance angle (symbol β)" means the angle from the illumination axis to the reference axis. The entrance angle is usually not larger than 90 but, for completeness, its full range is defined as 0 < β < 180. In order to specify the orientation in full, this angle is characterised by two components, β1 and β2;
Consistently using β1 and β2
GRE
IWG
SLR
Update of the definitions Correction of the Photometric Definitions
Reference document:
CIE Publication 54.2:2001 ”Retroreflection: Definition and measurement”
Page 3

## Slide 4
Definition of the Luminance Factor
Current: b
Proposal in GRE-83-26: RF
luminance factor (at a surface of a non-self-radiating medium in a given direction, under specified conditions of illumination) [βv]
NOTE For photoluminescent media, the luminance factor consists of 2 components: the reflected luminance factor, βv,R, and the luminescent luminance factor, βv,L. The sum of the reflected and luminescent luminance factors is the total luminance factor, βv,T: βv,T = βv,R + βv,L. The subscript R is used here for the reflected luminance factor because it is more intuitive than the traditional S and avoids confusion with the use of S to denote a state of polarization.
New proposal: bv,R
The luminance factor (symbol ) of a retroreflective device means the ratio of the tristimulus value Y of the sample and the tristimulus value of the perfect diffuser Yo.
GRE
IWG
SLR
Update of the definitions Correction of the Photometric Definitions
Reference document:
CIE Publication 54.2:2001 ”Retroreflection: Definition and measurement”
Page 4

## Slide 5
Annexes 13, 21 and 22 (current)
Weathering with xenon-arc weathering device
Evaluation by reference materials blue wool – grey scale
Annex 6 – Part 6 (new)
Weathering with xenon-arc weathering device
Defined time of 500 h
Evaluation by set up minimum level for specific coefficient of retroreflection at 80% of required values
Evaluation of colour as defined in R48
Replaced by
Justification
State-of-the-art test, defined parameters in referenced ISO 4892-2:2013
GRE
IWG
SLR
Page 5
Resistance to weathering

## Slide 6
Method applicable for retro-reflective sheeting material used for
  Retro-reflective markings of
  Classes C, D, E, F
  Classes 1, 2, 3, 4, 5
  and SMV Class 1 and 2
Method NOT applicable for retro-reflectors of
  Classes IA, IB, IIIA, IIIB and IVA
  Advance Warning Triangle of Type 1 and 2
GRE
IWG
SLR
Resistance to weathering
Page 6

## Slide 7
Adjustment of the sizes of the approval marks
  In Table 1, to reduce the number of minimum sizes of “a”: - the value “4 mm” will become “5 mm” - the value “12 mm” will become “8 mm”
Changes in the examples of the approval markings arrangement
  - Space removed for class IIIA
  - Size aligned
  - “104R” removed
  - “27R” replaced by WT
GRE
IWG
SLR
Arrangement of approval markings
Page 7

## Slide 8
Retro-reflective devices | Symbol | Minimum “a” in Annex 10 (in mm) | Paragraph
Retro-reflector for motor vehicles (independent) | IA | 5 | 5.1.
Retro-reflector for motor vehicles (combined with other signal lamps which are not watertight) | IB | 5 | 5.1.
Retro-reflector for trailers (independent) | IIIA | 5 | 5.1.
Retro-reflector for trailers (combined with other signal lamps which are not watertight) | IIIB | 5 | 5.1.
Wide-angle retro reflector | IVA | 5 | 5.1.
Conspicuity marking (material for contour/strip marking) | C | 8 | 5.2.
Conspicuity marking (material for distinctive markings/graphics intended for a limited area) | D | 8 | 5.2.
Conspicuity marking (material for distinctive markings/graphics intended for an extended area) | E | 8 | 5.2.
Conspicuity marking (materials for distinctive markings or graphics as base or background in printing process for fully coloured logos and markings of class "E" in use which fulfil the requirements of class "D" materials) | D/E | 8 | 5.2.
Retro-reflective materials for extremities marking of class F | F | 8 | 5.2.
Retro-reflective marking for long or heavy vehicles (retro-reflective and fluorescent materials) Marking plate of class 1 or class 2 | RF | 5 | 5.2.
Retro-reflective marking for long or heavy vehicles (retro-reflective only materials) Marking plate of class 3, class 4 or class 5 | RR | 5 | 5.2.
Marking for slow moving vehicles (retro-reflective and fluorescent materials) Marking plate of class 1 | RF | 5 | 5.2.
Marking for slow moving vehicles (retro-reflective only materials) Marking plate of class 2 | RR | 5 | 5.2.
Advance Warning Triangle (Type 1) | T1  WT1 | 8 | 5.3.
Advance Warning Triangle (Type 2) | T2  WT2 | 8 | 5.3.
Table 1
List of retro-reflective devices and their symbols

## Slide 9
E4
IIIA
150R01 216
a
a/2
a/3
a/3
a/3
E1
C
150R01
1148
E4
150R01 0216
IIIA
E4
150R01
IIIA 0216
E1
RF
150R01 22179
E3
WT1
150R01
4216
E3
WT2
150R01
4217
UPDATED DRAWINGS IN ANNEX 10
Page 9

## Slide 10
1 Communication
2 Minimum requirements for conformity of production control procedures
3 Minimum requirements for sampling by an inspector
4 Photometric measurements of retro-reflective devices and marking materials
5 Specifications of shape and dimensions
6 Resistance to heat
7 Resistance to water penetration for retro-reflective devices
8 Alternative test procedures of resistance to water penetration for retro-reflective devices of the Classes IB and IIIB
9 Resistance to fuels
10 Resistance to lubricating oils
11 Resistance to corrosion
12 Resistance of the accessible rear face of mirror-backed retro-reflective devices
13 Resistance to weathering
14 Stability of photometric properties
15 Resistance to cleaning in the case of a sample unit of retro-reflective marking devices
16 Bonding strength in the case of adhesive materials
17 Flexing - Retro-reflecting Markings
18 Resistance to impact
19 Rigidity of plates
20 Further test procedure for Advance Warning Triangles of Type 1 and 2
21 Arrangement of approval markings
22 Guidelines for installation of rear marking plates on slow-moving vehicles (by construction) and their trailers
23 Description of the measurement geometry for measurement of the daytime colour and the luminance factor of retro-reflective material
Page 10
GRE
IWG
SLR
Current structure of the Annexes in R150

## Slide 11
 | Annex Type of testing | Administrativ | Photom. measurment | Drawing | Chemical Test | Mechanical Test | Ad. Warning Triangle only | Environmental Test
1 | Communication |  |  |  |  |  |  | 
2 | Minimum requirements for conformity of production control procedures |  |  |  |  |  |  | 
3 | Minimum requirements for sampling by an inspector |  |  |  |  |  |  | 
4 | Photometric measurements of retro-reflective devices and marking materials |  |  |  |  |  |  | 
5 | Specifications of shape and dimensions |  |  |  |  |  |  | 
6 | Resistance to heat |  |  |  |  |  |  | 
7 | Resistance to water penetration for retro-reflective devices |  |  |  |  |  |  | 
8 | Alternative test procedures of resistance to water penetration for retro-reflective devices of the Classes IB and IIIB |  |  |  |  |  |  | 
9 | Resistance to fuels |  |  |  |  |  |  | 
10 | Resistance to lubricating oils |  |  |  |  |  |  | 
11 | Resistance to corrosion |  |  |  |  |  |  | 
12 | Resistance of the accessible rear face of mirror-backed retro-reflective devices |  |  |  |  |  |  | 
13 | Resistance to weathering |  |  |  |  |  |  | 
14 | Stability of photometric properties |  |  |  |  |  |  | 
15 | Resistance to cleaning in the case of a sample unit of retro-reflective marking devices |  |  |  |  |  |  | 
16 | Bonding strength in the case of adhesive materials |  |  |  |  |  |  | 
17 | Flexing - Retro-reflecting Markings |  |  |  |  |  |  | 
18 | Resistance to impact |  |  |  |  |  |  | 
19 | Rigidity of plates |  |  |  |  |  |  | 
20 | Further test procedure for Advance Warning Triangles of Type 1 and 2 |  |  |  |  |  |  | 
21 | Arrangement of approval markings |  |  |  |  |  |  | 
22 | Guidelines for installation of rear marking plates on slow-moving vehicles (by construction) and their trailers |  |  |  |  |  |  | 
23 | Description of the measurement geometry for measurement of the daytime colour and the luminance factor of retro-reflective material |  |  |  |  |  |  | 
Page 11

## Slide 12
1 Communication
2 Minimum requirements for conformity of production control procedures
3 Minimum requirements for sampling by an inspector
4 Photometric and colorimetric measurements
4.1 Photometric measurements of retro-reflective devices and marking materials
4.2. Description of the measurement geometry for measurement of the daytime colour and the luminance factor of retro-reflective material
4.3 Stability of photometric properties
5 Specifications of shape and dimensions
6 Environmental Testing
6.1 Resistance to heat
6.2 Resistance to water penetration for retro-reflective devices
6.3 Alternative test procedures of resistance to water penetration for retro-reflective devices of the Classes IB and IIIB
6.4 Resistance to corrosion
6.5 Resistance of the accessible rear face of mirror-backed retro-reflective devices
6.6 Resistance to weathering
7 Chemical Testing
7.1 Resistance to fuels
7.2 Resistance to lubricating oils
8 Mechanical testing
8.1 Resistance to cleaning in the case of a sample unit of retro-reflective marking devices
8.2 Bonding strength in the case of adhesive materials
8.3 Flexing - Retro-reflecting Markings
8.4 Resistance to impact
8.5 Rigidity of plates
9 Further test procedure for Advance Warning Triangles of Type 1 and 2
10 Arrangement of approval markings
11 Guidelines for installation of rear marking plates on slow-moving vehicles (by construction) and their trailers
Re-arrangement of the Annexes in R150
Page 12

## Slide 13
Update of definitions - Correction of the Photometric Definitions RI, RA, β1 , β2 , bv,R ,
Resistance to weathering 500 h xenon - retroreflection at 80% of required values
Arrangement of approval markings Adjustment of the sizes of the approval marks and changes in the examples of the approval markings arrangement
Updated drawings of Approval Markings Corrected and updated drawings
New arrangement of Annexes with grouped structure 23 Annexes re-arranged and grouped into 11 Annexes
Introduction of scientific notation
In order to assure that not more than 3 significant digits are shown for the required values
GRE
IWG
SLR
Summary of the main changes in Stage II, Step 1
Page 13