## Slide 1
Transmitted by the Chair and Secretary of VIAQ
Geneva, January 11-14, 2022
Chair: Andrey KOZLOV, Russian Federation
Co-Chair: Inji PARK, The Republic of Korea
Secretary: Andreas WEHRMEIER, BMW
Status Report of the
VIAQ (Vehicle Interior Air Quality)
Informal Working Group
Informal document GRPE-85-26-Rev.1
85th GRPE, 11-14 January 2022
Agenda item 12

## Slide 2
ToR for the Third Stage
Terms of reference and rules of procedure for the IWG on Vehicle Interior Air Quality
Informal document GRPE-81-09
Background. The group considered the inclusion in the scope of interior air pollutants from outside sources as a possible extension of the mandate at third stage. As an extension of the existing Mutual Resolution on VIAQ, this will take into account not only interior air emissions generated from interior materials and exhaust gases from the vehicle entering into the cabin but also outside air pollution sources. The list of outside air pollutions could include CO, NO, NO2, SO2, O3 volatile organic compounds (VOC), aldehydes, aromatic and aliphatic hydrocarbons, particulate number (PN) and mass (PM) and microbiological substances, e.g. allergens, fungi, bacteria and viruses. As an extension of the existing Mutual Resolution on VIAQ, this will take into account not only interior air quality but also the air cleaning efficiency of the vehicle air handling & treatment system.
Objective. This proposal expands on the issues of the vehicle interior air quality, addressing outside air pollutants entering into the vehicle cabin and the interior air cleaning efficiency, to develop a test procedure in a recommendation by including Part 4 in the Mutual Resolution No. 3.
Scope and work items. Outside air pollutants entering into the vehicle cabin and their cleaning efficiencies
(a) Collect the information and research data on relevant air pollutants and similar issues, and understand the current regulatory requirements with respect to vehicle interior air quality in different markets.
(b) Review, assess and develop new test procedures suitable for the measurement methods of air pollutants entering into the vehicle cabin and their cleaning efficiencies (including test modes, sample collection methods and analysis methods, etc.)
(c) Discuss the potential of air pollutants in the vehicle interior air with toxicologists.
(d) Develop a draft for test procedures in a recommendation.
Notes: 2

## Slide 3
VIAQ IWG Meetings since the last GRPE session
New vice-chair
23rd VIAQ IWG Meeting
  • Webex, 25th November 2021
  Half a day
New vice-chair of Informal Working Group was elected:
Inji Park, Chief Researcher
Korea Automobile Transportation Research Institute
Inji Park is in charge of vehicle interior air quality for new vehicles and Korean Green NCAP of VIAQ stream.
Notes: 3

## Slide 4
Timeline
2020 | 2021 | 2022 | 2023 | 2024 | 2025
81
GRPE
82
83
Data collection
Analysis of existing test procedures
Tests by VIAQ IWG members
Developing of harmonized test procedure
84
86
87
88
89
90
91
92
VIAQ
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
WP.29
197
PM Draft +Gas Draft Final Draft
Stage 3. Phase 1
Stage 3. Phase 2
85
Notes: 4

## Slide 5
Company | Presenter Name | Document Title | Document No.
KATRI | Inji Park | Effect of cabin ventilation mode on VIAQ during high PM episode in Korea | VIAQ-23-04
Fraunhofer IBP | Matthias Brunnermeier | Controllable lab test environment for assessing cabin air quality regarding PM2.5 and CO2 | VIAQ-23-05
AIR | Nick Molden | CEN Workshop 103: Validation of proposed cabin air quality assessment method – results of repeatability and reproducibility testing | VIAQ-23-06
NAMI | Andrey Kozlov | Measurement of inside and outside PM concentration with one DRX Aerosol Monitor | VIAQ-23-07
NAMI | Andrey Kozlov | The group feedback analysis regarding to test methodology, conditions, equipment | VIAQ-23-08 VIAQ-23-09
CERTAM | David Preterre | Reproduction of traffic pollution in a test bench to expose a whole car to reproducible scenario of urban pollution: IAQ devices and/or strategies assessment | VIAQ-23-10
UTAC | Nadir Hafs | Definition of protocol for vehicle in cabin air quality measurements | VIAQ-23-11
Information discussed last meeting

## Slide 6
Working items to develop new VIAQ test methodology
Vehicle Category
Criteria for excluding a vehicle from tests
Test Vehicle age/millage
Meteorological Conditions
Test Conditions
Sampling Points/Sampling Lines
Background air pollution level
Cabin air filter age
PM and gas components to be Measured
Measurement Methods
Test equipment requirements
Gas Analysers Calibration
Test Modes
HVAC Modes
Test Procedure
Test Protocol
The items
Notes: 6

## Slide 7
Feedback form
Notes: 7

## Slide 8
Responses from:
CLEPA
(EU Association of Supplier)
Korea Automobile Testing & Research Institute
CEN/WS 103*
OICA Members
UTAC/ESTACA
(Paris saclay)
CabinAir
Sweden AB
CabinAir
CLEPA
CEN
Korea
OICA
UTAC
The full text feedback tables are in the document VIAQ-23-09
*CEN/WS 103 items from the document “Real drive test method for collecting vehicle interior air quality data” // Doc. CEN/WS 103 N. 23, 2021
Notes: 8

## Slide 9
Working items
1. Vehicle Category (agreed)
Category 1-1
Notes: 9

## Slide 10
Working items
2. Criteria for excluding a vehicle from tests
Proposals:
Exclusion shall be based on a positive answer to any of the criteria below:
Is the vehicle more than one month aged?
Does the vehicle not have a full service history?
Is there a Malfunction Indication Light showing on the vehicle instrument panel?
Has the vehicle had unauthorised vehicle repairs?
Has any part of the vehicle’s heating and ventilation system replaced with non-original parts?
Through visual inspection of the vehicle, are there any damaged ventilation system relevant components?
Are there any obstructions to the vehicle air intake path?
Is the vehicle not in overall safe operating condition?
Is there any damage to the body of the vehicle, including but not limited to doors, windows and the rear?
Notes: 10

## Slide 11
Working items
3. Test Vehicle age/mileage
Proposals:
3 000…15 000 km
3 000…160 000 km
<25 000 km and age <2 years
>5 000 km
This item needs additional discussion
Notes: 11

## Slide 12
Working items
4. Meteorological Conditions
Proposals:
Weather condition: no rain, fog, snow or standing water on the carriageway
Relative Humidity 40…80%
Atmospheric pressure 85…110 kPa
Temperature:
-7…+35oC
10…20oC
5…25oC
Temperature range needs additional discussion
Notes: 12

## Slide 13
Working items
5. Test Conditions
Proposals:
The test must be primarily conducted on city roads and urban locations
Driving time Monday to Sunday, 06:00 to 20:00
Road condition Paved streets
It is recommended to avoid long tunnels, high altitudes and construction areas.
Each trip shall meet the conditions below:
Instantaneous vehicle speed ≤60 km/h
Minimum distance 10 km
Minimum duration 30 min
A normal driving style shall be adopted.
Average speed 40…60 km/h
Average altitude 0…700 m
There should the driver and one passenger present in the vehicle for the duration of the test.
All outer clothing of the driver should be made of [polyester] to minimise particle generation from the driver.
The cabin before the test should be cleaned and free of dust or other dirt.
The item needs additional discussion
Alternatively:
UN Requirements to RDE
Notes: 13

## Slide 14
Working items
6. Sampling Points/Sampling Lines
Proposals:
The interior sampling point should be a head-height between the front headrests
The external sampling point should be as close as reasonably possible to the ventilation air intake. Sampling should be isokinetic. Alternatively: Not measured, and used PM10 and PM2.5 data from real-time roadside monitoring stations
The sample lines should be made of a near-zero-loss material such as PTFE for gas and anti-static material for particulates. Not longer than 1 m and with no sharp bends.
The item needs additional discussion
Notes: 14

## Slide 15
Working items
7.Background air pollution level
Proposals:
PM2.5 concentration:
5…100 μg/m3
10…200 μg/m3
81…150 μg/m3
> 30 µg/m3
The item needs additional discussion
Notes: 15

## Slide 16
Working items
8.Cabin air filter age
Proposals:
HVAC filter age:
New, OEM-approved
Normal filters use for 3000 km or Ageing procedure
Original OEM HVAC filter with max. 3000 km
Aged filer out of filter replacement cycle which driving mileage 10 000 km∼15 000 km
Both New and Aged
The item needs additional discussion
Notes: 16

## Slide 17
Working items
9. PM and gas components to be Measured
Proposals:
PN (10 nm to 10 μm)
PM2.5
PM10
CO
CO2
NO2
The item needs additional discussion
Optionally:
small fraction PM (0.1-1 µm)
tVOC
PAH
NOx (NO2 & NO)
NH3
O3
Notes: 17

## Slide 18
Working items
10. Measurement Methods
Proposals:
PN concentration Condensation particle counter (10 nm to 10 μm)
PM concentration Mini Wide Range Aerosol Spectrometer
(<10 μm) Aethalometer
90° light scattering & filter-sampling
CO concentration Non-dispersive infra-red
Electrochemical cell
CO2 concentration Non-dispersive infra-red
NO2 concentration Non-dispersive ultra-violet
chemiluminescent detector
The item needs additional discussion in connection with item 9
Notes: 18

## Slide 19
Working items
11. Test equipment requirements
The item needs additional discussion in connection with items 9 and 10
Proposals:
PN concentration 0 to 1,000,000 #/cm3 (particles: 10 nm to 10 μm)
PM concentration (<2.5 μm) 0 to 1 mg/m3
PM concentration (<10 μm) 0 to 1 mg/m3
CO concentration 0 to 1 ppm
CO2 concentration 0 to 5,000 ppm
NO2 concentration 0 to 0.5 ppm
Alternatively:
PN concentration 1 to 2,000 #/cm3
PM concentration (<2.5 μm) 0 to 100 mg/m3
PM concentration (<10 μm) 0 to 100 mg/m3
NO2 concentration 0 to 2 ppb
Notes: 19

## Slide 20
Working items
12. Gas Analysers Calibration
Proposals:
For in-field calibration of the gas analysers, a zero and span calibration shall take place at the start of the test and a zero and span check shall be made at the end of each test that is under two hours in length. For tests longer than two hours, mid-test checks of zero or zero and span may be made (such that the time between checks does not exceed two hours); the analyser may be adjusted to the calibration gases if necessary.
Annual calibration following supplier recommendation
The item needs additional discussion
Notes: 20

## Slide 21
Working items
13. Test Modes
Proposals:
Urban (city) driving
Real driving conditions
Stationary test
Laboratory test
The item needs additional discussion
Notes: 21

## Slide 22
Working items
14. HVAC Modes
Proposals:
HVAC system settings:
Automatic mode (or for manual mode fan speed 50%/medium)
Temperature 21˚C (or for manual mode 50%/medium temperature)
Fresh air mode
Air conditioning switched ON
Ventilation flaps fully open and directed straight ahead
The item needs additional discussion
Alternatively:
Temperature 23°C
For manual HVAC: xx% fresh, yy% in recirculation
A/C must be OFF
Notes: 22

## Slide 23
Working items
15.Test Procedure
Proposals:
Cold start operation shall be excluded. To ensure this, the first 10 minutes or the first 2 km of driving under internal combustion engine operation shall be excluded from any test, whichever comes later. This restriction does not apply to vehicles with no internal combustion engine.
A test is a continuous stretch of driving that can contain multiple trips.
A test may be split up into multiple trips, each of which must meet the trip conditions. A trip shall start from a point at which the vehicle is stationary, with stationary defined as less than or equal to 0.5 km/h. There shall be no overlaps between the trips. A single trip shall be made up of continuous driving. Multiple trips from the same test can, in-between those trips, allow driving that does not meet the boundary conditions of CWA.
For test results to be deemed adequate for use in comparing interior air quality performance between models within the scope of this CWA, it shall be required to collect:
  at least 3 valid trips in total
  in the required fan speed/ventilation modes
  on 1 vehicle of its type.
The item needs additional discussion
Alternatively:
Measurements with two consecutive vehicles (the test is independent on background pollutant concentration)
Notes: 23

## Slide 24
Working items
16.Test Protocol
Proposals:
The protocol contains
Vehicle information (car registration number, mileage, engine type, filter type and age…)
Test condition information (testing date, driving locations, ambient conditions, number of passengers…)
Reporting of trip results (inside and outside measurement results, filtering efficiency…)
The item needs additional discussion
Notes: 24

## Slide 25
Additional research needed
Режим тестирования город, RDE, лаборатория… либо 2 типа тестов
Кондиционер
Температура в салоне
Рециркуляция
Ждать повышенных концентраций или ехать за грязным авто
Перечень компонентов, включать ли CO2 (токсикология)
Working Item | Research needed
4. Meteorological Conditions | Acceptable ambient temperature range
9. PM and gas components to be Measured | Which substances concentration to measure (takin into account their toxicity) Include or not CO2 (non toxic but affects on driver concentration and safety)
8. Cabin air filter age | What is more representative: New filter Aged filter Need to test both
13. Test Modes | Which combination of test modes is representative regarding VIAQ assessment: Urban (city) driving RDE (city + suburban + highway) Laboratory test
14. HVAC Modes | Which combination of HVAC settings is worst case: Air conditioner ON/OFF Interior temperature setting Recirculation ON/OFF
Notes: 25

## Slide 26
Next VIAQ IWG Meetings
24th VIAQ IWG Meeting (TBD)
  • Brussels, Belgium, April-May, 2022
  or Paris, France, April-May, 2022
  Two days
Notes: 26