## Slide 1: LCA Methodology for Automobile towards Worldwide Carbon Neutrality
Japan
Submitted by Japan
Informal document GRPE-86-17
86th GRPE, 30 May - 2 June 2022
Agenda item 14

## Slide 2: Proposal: LCA Activity at GRPE
Quote from
“Informal document GRPE-85-29 Rev.1”
Purpose
For towards to achieve carbon neutrality, assessment of the life cycle CO2 emission of automobiles needs to be clarified.
Aim
This activity aims to develop Carbon FootPrint - Product Category Rules for automobiles. (CFP-PCR (LCA Methodology))
The CFP-PCR formulated by this activity may be used by CPs of both the 1958 and the 1998 agreements or by automobile manufacturers, as a guideline to assess the life cycle CO2 emissions of automobiles for assistance in policy making or product development.

## Slide 3: Proposal : Scope at GRPE
Focus on discussion of methodology development
Item | Detail | Scope
Methodology (Product Category Rule) | Development of automotive LCA methodology Functional unit definition System boundary definition Activity/Intensity data definition Requirement to Primary data (include data format) Secondary data | ✓
Data Traceability System | Development of automotive LCA data traceability system Data platform definition Blockchain protocol definition Workflow for certification | NA
Comparisons (e.g. powertrain systems ) based on the newly developed harmonized methodology under GRPE activities may be one of the tool for regional policy making or product development.
Need further discussion regarding the LCA Regulatory requirements as a part of GRPE responsibilities

## Slide 4: Direction of new methodology
JAPAN is working on revision of automobile LCA methodology towards make it able to assess carbon neutrality activity.
 |  | Material Acquisition | Production | Distribution | Use | End of Life
JAMA 2011 | Activity data | Weight of material[kg] | Weight of processed material[kg] | Weight of distributed material[kg] | Fuel economy [km/L] Electricity economy [Wh/km] Lifetime milage[km] | Weight of Vehicle[kg]
 | Intensity | Material intensity [kg-CO2e/kg] | Process intensity [kg-CO2e/kg] | Distribution intensity [kg-CO2e/kg] | Fuel intensity [kg-CO2e/L] Electricity intensity [kg-CO2e/kWh] | Disposal intensity [kg-CO2e/kg]
Activity data (=weight of vehicle) cannot be ZERO. Need to develop methodology which intensity could be ZERO. |  |  |  |  |  | 
New Concept | Activity data | Weight of material[kg] | Energy of processed material[kWh] | Weight of distributed material[kg] | Fuel economy [km/L] Electricity economy [Wh/km] Lifetime milage[km] | Weight of recycled material[kg] Weight of disposed material[kg]
 | Intensity | Material intensity [kg-CO2e/kg] | Energy intensity [kg-CO2e/kWh] | Distribution intensity [kg-CO2e/kg] | Fuel intensity [kg-CO2e/L] Electricity intensity [kg-CO2e/kWh] | Recycle intensity [kg-CO2e/kg] Disposal intensity [kg-CO2e/kg]
※blue : Primary data

## Slide 5: Conclusion
Urgent
  It is urgent that fight against climate change.
Life cycle perspective
  Towards carbon neutrality, it became more important to consider in life cycle perspective.
Automobile LCA method in JAPAN
  In JAPAN we already developed transparency Automobile LCA method.
  It’s able to assess CO2 emissions, but now, we would like to assess activities which towards carbon neutrality.
Worldwide harmonize
  Carbon neutrality cannot be achieved without worldwide government and private enterprise cooperation.
  Let’s discuss LCA methodology for Automobile at GRPE.