## Slide 1
Automated and connected road transport
Regulatory framework in France
Latest developments
Website : https://www.ecologie.gouv.fr/en/automated-vehicles
Transmitted by the expert from France Informal document GRVA-14-22 14th GRVA, 26–30 September 2022
Provisional agenda item 11

## Slide 2
National regulatory framework for deployment
2019 Mobility Law + 2021 Ordinance and Decree + 3 orders (intervention operator and approved qualified bodies)
  Definitions
    automation = delegation to a driving system (partial if handover requests anytime)
    automated road transport system (ARTS) = automated vehicles + remote capabilities
    remote intervention = capabilities to order and acquit automated manoeuvers
  Liability : automated system responsible if active (unless driver fails to takeover)
  Autorisation process for ARTS (highly or totally automated vehicles integrated in a technical system, deployed on predefined route or zone)
Vehicle
System ↔ Zone ↔ Operation
Service
Type approval Safety demonstration + Third party advice Commissioning Monitoring
Entry into force : 1st September 2022
Notes: Préciser différence entre highly et totally
8.1. Véhicule partiellement automatisé : véhicule équipé d'un système de conduite automatisé exerçant le contrôle dynamique du véhicule dans un domaine de conception fonctionnelle particulier, devant effectuer une demande de reprise en main pour répondre à certains aléas de circulation ou certaines défaillances pendant une manœuvre effectuée dans son domaine de conception fonctionnelle ; 8.2. Véhicule hautement automatisé : véhicule équipé d'un système de conduite automatisé exerçant le contrôle dynamique d'un véhicule dans un domaine de conception fonctionnelle particulier, pouvant répondre à tout aléa de circulation ou défaillance, sans exercer de demande de reprise en main pendant une manœuvre effectuée dans son domaine de conception fonctionnelle. Ce véhicule peut être intégré dans un système technique de transport routier automatisé tel que défini au 1° de l'article R. 3151-1 du code des transports ; 8.3. Véhicule totalement automatisé : véhicule équipé d'un système de conduite automatisé exerçant le contrôle dynamique d'un véhicule pouvant répondre à tout aléa de circulation ou défaillance, sans exercer de demande de reprise en main pendant une manœuvre dans le domaine de conception technique du système technique de transport routier automatisé auquel ce véhicule est intégré, tels que définis aux 1° et 4° de l'article R. 3151-1 du code des transports

## Slide 3
National policy for deployment
Order of 2 August 2022 implementing Article R. 3152-3 of the Transport Code on the authorisation of remote participants in road transport systems
https://www.legifrance.gouv.fr/jorf/id/JORFTEXT000046151685
Order of 2 August 2022 in application of article R. 3152-30 of the transport code, relating to the approval procedure for qualified organisations
https://www.legifrance.gouv.fr/jorf/id/JORFTEXT000046216833
Order of 5 August 2022 taken in application of article R. 3152-24 of the transport code relating to the content of the opinions of approved qualified organisations
https://www.legifrance.gouv.fr/jorf/id/JORFTEXT000046174400
Decree No. 2022-1034 of July 21, 2022 publishing the amendment to the Vienna International Convention on Road Traffic of 8 November 1968, adopted in Geneva on 14 January 2022
https://www.legifrance.gouv.fr/jorf/id/JORFTEXT000046081252

## Slide 4
French safety demonstration architecture
Vehicle
Technical system
= vehicle + equipments + control center
Approved by a type approval authority
Approved qualified third party advice
Decision of the service organizer
System
= technical system + route
+ operating and maintenance rules
In-service operation
Monitoring + Audit
Commissioning
Fields
Validation approach
1.
2.
3.
4.
5.
4

## Slide 5
FR and UN/EU regulations
Vehicle(s)
System
Service
including remote intervention, connectivity, …
+ external capabilities
Validation architecture
in a predefined route / zone
Vehicle type approval
UN or EU Regulation for vehicles equipped with automated driving systems (ADS) international categories (M and N)
French order on national categories (urban shuttles)
Technical system validation
If the system includes a remote operator, UN or EU ADS regulation to specifie capabilities, comparable to the French ARTS decree
French ARTS decree sets procedures and roles
ARTS validation
1.
2.
3.
Notes: Question sur bloc 1 « external capabilities » : capabilities of the vehicle to receive and emit signal to infrastructure (lights, supervision center, …) or other vehicles to extend capabilities
UN or EU regulation to specifie capabilities : explain

## Slide 6
FR – UN/EU : use cases covered by regulation
French decree (system+service-oriented) | UN or EU ADS Regulation (vehicle-oriented) WP29/GRVA FRAV work
Automated road transport system (ARTS) Highly or fully automated vehicles and their technical installations (technical system) Deployed in a predefined route or zone for a transport service, both public and private For the carriage of passengers NB : freight and logistics = forthcoming | Vehicles type approval Highly or fully automated vehicles, including dual modes vehicles Fully automated vehicles designed and constructed for use on a predined area or on a predefined route with fixed start and end points of a journey/trip For the carriage of passengers or goods

## Slide 7
FR – UN/EU : safety requirements and demonstration
UN VMAD or EU ADS regulation sets requirements on safety, demonstration methods (tests) and documentation for automated vehicles
FR regulation sets
drivers / remote operator roles and responsabilities
general safety requirements on automated systems
requirements on safety demonstration procedures
Safety demonstration guidance will need to be developped accordingly, e.g :
Scenario-based approach for validation
Reference safety target
Remote intervention functions characterisation
Route or zone characterisation
….

## Slide 8: Safety standards for automated transport systems 1/3: published documents
Theme / title | Document | State | Remarks (EN versions for recent methodological documents)
Horizontal regulation - use case approach | Methodological document DGITM | Published 2017 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Automated-vehicle-horizontal-regulation-2017-EN.pdf
New safety validation methods | Methodological document DGITM-PFA | Published2020 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Nouvelle-approche-validation-systemes-avril-2019-EN.pdf
Human/system articulation: manoeuvre approach | Methodological document DGITM | Published 2020 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_AD-articulation-roles-systemes-octobre-2020-EN.pdf
Characterisation of the routes: division into sections | Research report UGE-STRMTG | Published 2021 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_STPA-analyse-securite-parcours-mars-2021-EN.pdf
Application of the GAME approach | Implementation Guide STRMTG | Published 2021 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Guide-application-STRA-principe-GAME-EN.pdf
Scenario-based validation approach | Methodological document DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Approche-par-scenarios-fevrier-2022-EN.pdf

## Slide 9: Safety standards for automated transport 2/3: methodological documents to come
Theme / title | Document | Deadline | Remarks
Scenario validation: interactions with law enforcement and priority vehicles | Methodological framework document DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM_Approche-par-scenarios-fevrier-2022-EN.pdf
Accidentology references for safety objectives | Research report DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM-Rapport_accidentalite-juillet_2022-EN.pdf
ODD definition | Methodological framework document DGITM | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM-ODD_dezscriptors-juin_2022-EN.pdf
Route characterisation | Methodological framework document DGITM | Q3 2022 | Will incorporate elements from the ODD document and the "route cutting" study report. To be integrated into the STRMTG GAME safety demonstration guide (see below)
Characterisation of remote intervention functions | Methodological framework document DGITM | Q3 2022 | To be integrated into the STRMTG GAME safety demonstration guide (see below)
Scenario generation | Methodological framework document DGITM-SystemX | Published 2022 | https://www.ecologie.gouv.fr/sites/default/files/DGITM-L1-septembre_2022-EN.pdf
Scenario rating |  | Q3 2022 | To be included in the STRMTG GAME safety demonstration guide (see below)
Use of scenarios in the safety demonstration |  | Q4 2022 | 

## Slide 10: Safety standards for automated transport systems 3/3: forthcoming guidance
Theme / title | Document | Deadline | Remarks
GAME safety demonstration Definitions from the glossary Safety demonstration method, including: Pathway decomposition Functional decomposition Hazards and high level requirements | Implementation Guide STRMTG | Published | https://www.ecologie.gouv.fr/sites/default/files/DGITM-GuideD%C3%A9monstration_GAME_STRA_v1_31aout2022-EN.pdf
Additions to be considered in the short term: Use of scenarios and safety analysis of routes | STRMTG | 2023 | 
RETEX - Handling of events | Implementation Guide STRMTG | 2023 | 
Cyber requirements | Implementation Guide STRMTG | Q4 2022 | NB: The STRMTG is aiming for a 'martyr' version of this guide by Q3 2022
Missions of the accredited qualified bodies | Implementation Guide STRMTG | Q3 2022 |