## Slide 1: Approval process of LED replacement light sources
2022-09-26
Ph. Plathner, W. Schlager
Submitted by the experts from IEC
Informal document GRE-87-02
(87th GRE, 25-28 October 2022, agenda item 5.)

## Slide 2: Content
UN approval process
National approval process
Summary and request for guidance

## Slide 3: UN R37 approval full photometric equivalence according to guideline (GRE-83-15)
PRO‘s
  complete set of light source specifications based on “full equivalence” to incandescent technology
    Possible for 5W types with today LED technology
    Possible for 10W and 20W types in near / mid future
  Leads to same photometric performance in the application
  No need for testing in the luminaire (no need for positive list)
CON‘s
  none
Example 1: Signalling light source C5W (low power)
Far field: filament-like
Near field: filament-like

## Slide 4: UN R37 approval full photometric equivalence according to guideline (GRE-83-15)
PRO‘s
  complete set of light source specifications based on “full equivalence” to incandescent technology
    But not technically feasible today for high flux categories
  It would …
    lead to same beam performance
    mean no headlamp testing, no positive list needed
CON‘s
  Full equivalence (= emulation of filament) would not improve the beam performance, i.e. advantages of LED technology not utilised
Example 2: Road illumination light source H7 (high flux)
Far field: filament-like
Homogeneous illumination
of whole reflector (green and red segments)
full-equivalence solutions not feasible for high flux categories
with todays LED technology
from
reflector segment to
light on the road

## Slide 5: National approvals (Germany, France, Austria …) Deviating from full photometric equivalence
Methodology
  Extensive testing (in headlamps and vehicles)
  Limited light source specifications
  Resulting in positive list
PRO‘s
  Enabling legalization of safe LEDr, supporting market surveillance
  Increased beam performance in many tested headlamps
  Technically feasible with today LED technology
CON‘s
  Incompatible with some headlamps / vehicles
  Mis-use may lead to non-compliant beams
  High effort for industry and approval authorities to maintain the positive list
  Country-specific approval processes, limited mutual recognition
  Not yet possible in most countries
Less light in green segments
More light in red segments
from
reflector segment to
light on the road

## Slide 6
LEDr acc. to R37 with full photometric equivalence
Filament bulb acc. to R37
* Besides the color temperature
 SAME* beam performance with both technologies
Nationally approved LEDr,
deviating from full-equivalence
Filament bulb acc. to R37
*Compliant beam with more light in 50m … 70 m range
Examples – beam performance comparison
 BETTER* beam performance with LEDr
=
>
 BETTER beam performance with LEDr
 SAME beam performance with both technologies

## Slide 7: Summary and request for guidance
SUMMARY:
  The UNECE R37 Framework for LEDr is based on “full photometric equivalence” and is enforced. It allows safe LED replacements with the SAME photometric performance as the conventional technology.
  For road illumination, a further extension of the framework can offer BETTER beam performance:
    Overcome the limitations and drawbacks of the conventional light source
    Make full use of the advantages of LED technology
  National-approved 2-sided designs have proven that compliant and better performing beams are feasible.
    Data from German and French approvals are public.
    The basis for the national approvals is always a verification of the photometry in the application (positive list approach)
REQUEST FOR GUIDANCE:
  Does GRE support the re-evaluation of the equivalence criteria beyond full-equivalence?