## Slide 1: Reference Fuels: Diesel Cloud Point
Changed standard with UN R154
Submitted by the expert of OICA Informal document GRPE-87-12 87th GRPE, 10 - 13 January 2023 agenda item 3.(a).

## Slide 2: Reference Fuels: Diesel Cloud Point
Diesel (B7) Reference Fuel properties are described within…
However, EN 116 describes the test method for the “Cold Filter Plugging Point (CFPP)”, not the “Cloud Point (CP)”.
CP*: “Temperature below which paraffin wax in diesel or biowax in biodiesels forms a cloudy appearance”
CFPP**: “Lowest temperature at which a given volume of diesel passes through a standardized filtration device in a specified time when cooled under certain conditions”
As EN 23015 was withdrawn / replaced the correct test method should be EN ISO 3015, not EN 116.
*: https://en.wikipedia.org/wiki/Cloud_point
**: https://en.wikipedia.org/wiki/Cold_filter_plugging_point
For the “Cloud Point”, the reference test method differs between UN-R154, UN-R83/07, UN-R83/06 and (EU) 2017/1151 :
Paragraph 5.4. of Annex B3 to UN-R154 for Level 1A
Paragraph 1.2. of Annex 10 to UN-R83/07 and 06
Paragraph 2. of Annex IX to (EU) 2017/1151
EU
UN
Fuel | Regulation | Parameter | Unit | Limits |  | Test Method
 |  |  |  | Minimum | Maximum | 
Diesel B7 | UN-R154 | Cloud Point | °C | - | -10 | EN 116
Diesel B7 | UN-R83/07 | Cloud Point | °C | - | -10 | EN 23015
Diesel B7 | UN-R83/06 | Cloud Point | °C | - | -10 | EN 23015
Diesel B7 | 2017/1151 | Cloud Point | °C | - | -10 | EN 23015

## Slide 3: Reference Fuels: Diesel Cloud Point
Fuel | Regulation | Parameter | Unit | Limits |  | Test Method
 |  |  |  | Minimum | Maximum | 
Diesel B7 | UN-R154 | Cloud Point | °C | - | -10 | EN 116
Diesel B7 | UN-R83/07 | Cloud Point | °C | - | -10 | EN 23015
Diesel B7 | UN-R83/06 | Cloud Point | °C | - | -10 | EN 23015
Diesel B7 | 2017/1151 | Cloud Point | °C | - | -10 | EN 23015
Specifications for „Cloud Point“:
Fuel | Regulation | Parameter | Unit | Limits |  | Test Method
 |  |  |  | Minimum | Maximum | 
Diesel B5 | UN-R83/07 | CFPP | °C | - | -5 | EN 116
Diesel B5 | UN-R83/06 | CFPP | °C | - | -5 | EN 116
Diesel / B0 / B5 | UN-R83/05 | CFPP | °C | - | -5 | EN 116
Specifications for „Cold Filter Plugging Point“: