## Slide 1
Transmitted by the Chair and Secretary of VIAQ
Geneva, 10 – 13 January, 2023
Chair: Andrey KOZLOV, Russian Federation
Co-Chair: Inji PARK, The Republic of Korea
Secretary: Andreas WEHRMEIER, BMW
Status Report of the
VIAQ (Vehicle Interior Air Quality)
Informal Working Group
Informal document GRPE-87-47
87th GRPE, 10 – 13 January 2023
Agenda item 12

## Slide 2
ToR for the Third Stage
Terms of reference and rules of procedure for the IWG on Vehicle Interior Air Quality
Informal document GRPE-81-09
Background. The group considered the inclusion in the scope of interior air pollutants from outside sources as a possible extension of the mandate at third stage. As an extension of the existing Mutual Resolution on VIAQ, this will take into account not only interior air emissions generated from interior materials and exhaust gases from the vehicle entering into the cabin but also outside air pollution sources. The list of outside air pollutions could include CO, NO, NO2, SO2, O3 volatile organic compounds (VOC), aldehydes, aromatic and aliphatic hydrocarbons, particulate number (PN) and mass (PM) and microbiological substances, e.g. allergens, fungi, bacteria and viruses. As an extension of the existing Mutual Resolution on VIAQ, this will take into account not only interior air quality but also the air cleaning efficiency of the vehicle air handling & treatment system.
Objective. This proposal expands on the issues of the vehicle interior air quality, addressing outside air pollutants entering into the vehicle cabin and the interior air cleaning efficiency, to develop a test procedure in a recommendation by including Part 4 in the Mutual Resolution No. 3.
Scope and work items. Outside air pollutants entering into the vehicle cabin and their cleaning efficiencies
(a) Collect the information and research data on relevant air pollutants and similar issues, and understand the current regulatory requirements with respect to vehicle interior air quality in different markets.
(b) Review, assess and develop new test procedures suitable for the measurement methods of air pollutants entering into the vehicle cabin and their cleaning efficiencies (including test modes, sample collection methods and analysis methods, etc.)
(c) Discuss the potential of air pollutants in the vehicle interior air with toxicologists.
(d) Develop a draft for test procedures in a recommendation.
Notes: 2

## Slide 3
25th VIAQ IWG Meeting (on-line)
  • Teams, 9th November 2022
  Half a day
26th VIAQ IWG Meeting (hybrid)
  • Geneva, Switzerland, 10th January, 2023
  • Half a day
VIAQ IWG Meetings since the last GRPE session
Notes: 3

## Slide 4
Timeline
2020 | 2021 | 2022 | 2023 | 2024 | 2025
81
GRPE
82
83
Data collection
Analysis of existing test procedures
Tests by VIAQ IWG members
Developing of harmonized test procedure
84
86
87
88
89
90
91
92
VIAQ
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
WP.29
197
PM Draft +Gas Draft Final Draft
Stage 3. Phase 1
Stage 3. Phase 2
85
Notes: 4

## Slide 5
Information presented 25th meeting
Company | Presenter Name | Document Title | Document No.
KOTSA | Inji Park | Behavior of particulate matters measured in vehicle cabin during real driving conditions | VIAQ-25-04
Airlib | Herve Borrel | Improved in-cabin air quality with map-based air recirculation control | VIAQ-25-05
UTAC/ESTACA | Amine Mehel | Simultaneous in-cabin and on-road CO2 concentrations during on-board mobile measurements | VIAQ-25-06
NAMI | Andrey Kozlov | Test methodology development and repeatability assessment | VIAQ-25-07
UTAC/ESTACA | Nadir Hafs | The necessity of laboratory test in stabilized controlled atmosphere for vehicle in-cabin air quality full characterization | VIAQ-25-08
CLEPA | Markus Michael | Comments on UN VIAQ IWG 24th session | VIAQ-25-09 VIAQ-25-10

## Slide 6
Information presented 26th meeting
Company | Presenter Name | Document Title | Document No.
UTAC | Hanaa Er-rbib | Test Equipment requirements: Proposal | VIAQ-26-04
Freudenberg filtration technologies | Ulrich Stahl | Artificial ageing of cabin air filters | VIAQ-26-05
UTAC/ESTACA | Nadir Hafs, Amine Mehel | Laboratory tests for vehicle in-cabin air quality characterization: their complementarities to on-road tests | VIAQ-26-06
Cambustion | Mark Peckham & Jamie Parnell | Measurement of real time NO & NO2 in cabin inlet air flow in a “chase” vehicle | VIAQ-26-08

## Slide 7
Discussion of working items
The purpose of this discussion was to formulate tasks for farther group activities and to develop harmonized PM measurement test method
Vehicle Category
Criteria for excluding a vehicle from tests
Test Vehicle age/millage
Meteorological Conditions
Test Conditions
Sampling Points/Sampling Lines
Ambient air concentration level
Cabin air filter age
PM and gas components to be Measured
Measurement Methods
Test equipment requirements
Gas Analysers Calibration
Test Modes
HVAC Modes
Test Procedure
Test Protocol
The items
Notes: 7

## Slide 8
Working items
1. Vehicle Category (agreed)
Category 1-1
Notes: 8

## Slide 9
Working items
2. Criteria for excluding a vehicle from tests (agreed)
Exclusion shall be based on a positive answer to any of the criteria below:
Does the vehicle not have a full service history?
Is there a Malfunction Indication Light showing on the vehicle instrument panel?
Has the vehicle had unauthorised vehicle repairs?
Has any part of the vehicle’s heating and ventilation system replaced with non-original parts?
Through visual inspection of the vehicle, are there any damaged ventilation system relevant components?
Are there any obstructions to the vehicle air intake path?
Is the vehicle not in overall safe operating condition?
Is there any damage to the body of the vehicle, including but not limited to doors, windows and the rear?
Notes: 9

## Slide 10
Working items
3. Test Vehicle age/mileage (agreed)
Test vehicle age: more than one month
Test vehicle mileage: 3 000…15 000 km
Notes: 10

## Slide 11
Working items
4. Meteorological Conditions (agreed)
Weather condition: no rain, fog, snow or standing water on the carriageway
Relative Humidity: 40…90%
Atmospheric pressure: 85…110 kPa
Temperature: +5…+25oC
Notes: 11

## Slide 12
Working items
5. Test Conditions
The VIAQ performance shall be demonstrated by testing vehicles on the road, operated over their normal driving patterns, conditions and payloads. The test shall be conducted on paved roads (e.g. off-road operation is not permitted).
Windows, doors, sunroof or convertible soft top must be closed at all times. Heated or cooled seats should not be used.
When cleaning the vehicle prior to testing, only a damp cloth should be used. Fragrances and air fresheners should be avoided.
There should the driver and one passenger present in the vehicle for the duration of the test. All outer clothing of the driver and passenger should be made of polyester to minimize particle generation from the driver. Clothing should cover both arms and legs.
The occupants should avoid applying any fragrances or make-up prior to or during the test. Further, occupants should not have smoked for at least 24 hours before a test.
Notes: 12

## Slide 13
Working items
5. Test Conditions
The trip shall consist of approximately 55 per cent urban and 45 per cent expressway speed bins. ‘Approximately’ shall mean the interval of ±10 per cent points around the stated percentages. The urban speed bin however can be lower than 45 per cent but never be less than 40 per cent of the total trip distance.
Urban speed bin is characterised by vehicle speeds lower than or equal to 60 km/h.
Expressway speed bin is characterised by speeds above 60 km/h and up to 100 km/h.
Local speed limits remain in force during a test, notwithstanding other legal consequences. Stop periods, defined by vehicle speed of less than 1 km/h, shall account for 6-30 per cent of the time duration of urban operation. Urban operation may contain several stop periods of 10 s or longer.
The trip duration shall be between 30 and 60 minutes. The trip distance - TBD.
The start and the end points of a trip shall not differ in their elevation above sea level by more than 100 m. In addition, the proportional cumulative positive altitude gain over the entire trip and over the urban operation shall be less than 1,200 m/100 km.
*Requirements regarding: Working document ECE/TRANS/WP.29/GRPE/2023/3 “Proposal for a new UN Regulation No. [XXX] on uniform provisions concerning the approval of light duty passenger and commercial vehicles with regards to real driving emissions (RDE)”
Notes: 13

## Slide 14
Working items
6. Sampling Points/Sampling Lines
The interior sampling point should be a head-height between the front headrests
The external sampling point should be as close as reasonably possible to the ventilation air intake.
3. The sampling lines to the analyzer should be:
  as short as possible
  line lengths must be identical and not more than 1 m
  with few bendings as possible
  with no sharp bendings
  made of antistatic materials for particles measurement
  made of PTFE for gases measurement
  with diameter compatible to measurement equipment, usually 6 mm or 8 mm (outer diameter)
Notes: 14

## Slide 15
Working items
7. Ambient air concentration level
PM2.5 concentration should be not less than 30 µg/m3 and not more than 500 µg/m3
Task: The group need to set background levels to all measured components (regarding item 9)
NO - TBD
NO2 - TBD
CO2 - TBD
Notes: 15

## Slide 16
Working items
8. Cabin air filter age
HVAC filter age:
OEM-approved filter artificially aged to 3000 km
If a vehicle is not installed with a filter by the OEM, the vehicle to be tested with no filter present.
Task: Define artificial filter aging procedure, if good procedure is available only take artificial aged filter
Notes: 16

## Slide 17
Working items
9. PM and gas components to be Measured
PM2.5
NO
NO2
CO2 (Interior only)
Task: Check real NO2 and NO concentration in outside air
Notes: 17

## Slide 18
Working items
10. Measurement Methods (agreed)
PM concentration Optical particle counter
NO and NO2 concentration Chemiluminescent detector
CO2 concentration Non-dispersive infra-red
Notes: 18

## Slide 19
Working items
11. Test equipment requirements
Task: Prepare specification for test equipment
PM2.5 concentration 0.001 to 0.5 mg/m3
NO concentration 0 to 0.5 ppm
NO2 concentration 0 to 0.5 ppm
CO2 concentration 0 to 5,000 ppm
Time resolution: <2 s
Notes: 19

## Slide 20
Working items
12. Gas Analysers Calibration (agreed)
Calibration and linearization of the equipment shall be performed according to manufacturer recommendations prior to the commencement of measurements.
After the equipment is installed in the vehicle, a dynamic calibration shall be performed. The dynamic calibration ensures that the paired instruments are measuring the same concentrations. The dynamic calibration should be run each time: before the test series; if there is a new or changes to an existing test equipment installation on a vehicle; and after the first test to ensure in correct measurement. For the purposes of this calibration test, a stainless steel Y-piece should be used to split the air from the exterior sample probe equally between the interior and exterior measurement instruments. At the end of the calibration, the Y-piece should be removed and the installation returned to the test configuration.
The dynamic calibration test should be run for at least 30 minutes and expose the vehicle to concentrations in the range defined in item 7. The Pearson correlation coefficient between the data points from each matched pair of measurement devices shall be calculated. For a valid calibration, the r2 on all devices should be at least 0.98.
The drift of the zero response of the particle number instruments, defined as the mean response to HEPA filtered air at the inlet of the sampling line during a time interval of at least 30 seconds, shall be tested prior to each test and shall be less than 3 mg/m3.
The drift of the zero response of the carbon dioxide instruments, defined as the mean response to ambient air at the inlet of the sampling line during a time interval of at least 30 seconds, shall be tested prior to each test and shall be 413 ppm ±20 ppm.
Annual calibration following supplier recommendation.
Notes: 20

## Slide 21
Working items
13. Test Modes
Real driving conditions (urban + urban motorway)
Laboratory test (see VIAQ-22-11, VIAQ-23-05, VIAQ-23-10, VIAQ-23-11, VIAQ-24-05, VIAQ-25-08, VIAQ-26-06)
Notes: 21

## Slide 22
Working items
14. HVAC Modes
HVAC settings should be as automatic as possible. However, some vehicles do not provide automatic settings, or automatic settings can be adjusted.
A) Start to set HVAС to automatic. If vehicle does not have an automatic HVAC program or automatic settings can be adjusted follow the next steps:
B) Set temperature to 22˚C or 50% (medium) temperature setting
C) Set fan speed to 50% (medium)
D) Switch air conditioning: ON (need clarification from OICA)
E) Switch ventilation flaps: fully open and directed straight ahead;
F) Switch air quality sensors: ON
G) Switch ionization: ON
H) Do not use fragrance programs
OICA proposals
Notes: 22

## Slide 23
Working items
15. Test Procedure (PM measurement)
1. Measure ambient air temperature, relative humidity, pressure and background air pollutants concentration.
2. Start the engine, adjust HVAC operation mode, switch on the PM analyzers and drive for at least 10 min.
3. Drive to the beginning of the test rote, start PM analyzers, GPS logger.
4. Drive on the rote urban and expressway parts.
5. Park the car, stop the PM measurement, GPS logger.
6. Switch off PM analyzer and the engine.
7. Save measurement protocols from PM analyzers and GPS track from logger to the computer.
8. Take another background measurement according to subclause 1. Vehicle real driving test is complete.
Notes: 23

## Slide 24
Working items
16. Test Protocol
The protocol contains
Vehicle information (type, variant, version, manufacturer, mileage, engine type, fuel type, filter type and date of installation…)
Test condition information (testing date, test locations, test time, test equipment…)
Reporting of test results (inside and outside concentrations measurement results, ventilation mode, ambient conditions, mean vehicle speed, test distance, altitude, filtering efficiency…)
Task: This item must further be updated, when test procedure will be finalized
Notes: 24

## Slide 25
Draft of Part IV of the Mutual Resolution (M.R.3)
Draft document (VIAQ-26-07r1)
Contents
Purpose
Scope and application
Definitions
Abbreviations
General provisions
Normative references
Requirements for the test vehicle
Requirements for the test apparatus, instrument and equipment
Test procedure, test mode, and test conditions
Calculation, presentation of results, precision and uncertainty
Performance characteristics
Quality assurance/quality control
Annex 7. Test report of emissions entering to the vehicle cabin with outside air pollutants and the interior air cleaning efficiency
Notes: 25

## Slide 26
List of tasks
Working Item | Tasks
7. Ambient air concentration level | The group need to set background levels to all measured components (regarding item 9)
8. Cabin air filter age | Define artificial filter aging procedure, if good procedure is available only take artificial aged filter
9. PM and gas components to be Measured | Check real NO2 and NO concentration in outside air
11. Test equipment requirements | Prepare specification for test equipment
16. Test Protocol | This item must further be updated, when test procedure will be finalized
Drafting work | Send out Draft document*, collect and analyze comments, revise the draft document
* The Draft Part IV of the Mutual Resolution (M.R.3) on Vehicle Interior Air Quality (VIAQ-26-07r1)
Notes: 26

## Slide 27
Next VIAQ IWG Meetings
27th VIAQ IWG Meeting (TBD)
  Paris, France, May, 2023
  Two days
Notes: 27