## Slide 1
1
Research on Measurement Methods for
HDV in Multiple Driving Mode Conditions
China Automotive Technology and Research Center Co., Ltd.
7-10th February 2023, GRBP 77th Session
Dongming XIE1, Yanning CHANG1, Yu LIU1, Xi HU1, Jiewei LIN2, Yue WANG3
1. China Automotive Technology and Research Center Co., Ltd., 2. Tianjin University, 3. Beiqi Foton Motor Co., Ltd.
- CATC Data Study and Measurement Methods Research -
Informal document GRBP-77-28
Notes: 1

## Slide 2: Review
2
June, 2020, China introduced “Measurement Methods for Noise Emitted by Light-duty Vehicles in Multiple Driving Mode Conditions” in the 16th ASEP IWG meeting.
August, 2021, the project GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions” launched.
October, 2021, GB/T 40578-2021 “Measurement Methods for Noise Emitted by Light-duty Vehicles in Multiple Driving Mode Conditions” published.
September, 2022, HDV working condition survey conducted for the measurement methods based on CATC data.
January, 2023, GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions” began soliciting public opinion.

## Slide 3
GB/T 40578-2021 for LDV
cruise noise
Acceleration noise
Cruise noise
Test speeds (km/h) | VPP'=30±1 | VPP'=50±1 | VPP'=70±2
Engine speeds (r/min) | nBB'=Idle to 80%S |  | 
Acceleration (m/s2) | 0.5≤atest≤3.5 | 0.5≤atest≤3.0 | 0.3≤atest≤2.5
Test Gears | (1+X/2)/2+1 | (1+X/2) | (X+X/2)/2+1
 | D for unlockable |  | 
Accelerator Position | POT or WOT (Both are possible) |  | 
Noise Tested | Lmax per run for left side and right side separately |  | 
No. of Runs* | 2 |  | 
Intermediate Result | Average of per side |  | 
Final result | Higher one of averages |  | 
*M1 (PMR≥90 kW/t), 2 runs can be added at different acceleration. |  |  | 
Test speeds (km/h) | VPP'=80±2 | VPP’=110±2 for M1 VPP’=90±2 for others
Engine speeds (r/min) | nBB'=Idle to 80%S | 
Acceleration (m/s2) | atest≤0.15 | 
Test Gears | Highest lockable gear or D for unlockable | 
Accelerator Position | POT (Cruise) | 
Noise Tested (dB(A)) | Lmax per run for left side and right side separately | 
No. of Runs | 2 | 
Intermediate Result | Average of per side | 
Final result | Higher one of averages | 
3

## Slide 4
 | Bus | Coach | Heavy Truck | Light Truck | Dumper | Tractor
Fleet Size | 13 | 12 | 15 | 12 | 10 | 14
Distance (10000 km) | 43.74 | 28.14 | 23.22 | 13.23 | 13.46 | 29.63
City | 16 cities |  |  |  |  | 
Vocation | Intercity Long Haul, Local Delivery, City Construction, Passenger Transportion… |  |  |  |  | 
Established a fleet composed of 76 heavy-duty vehicles, covering typical vehicle types, vocations and cities all over China.
Collected 1hz real-time data including vehicle speed, engine speed and other parameters by free driving operation.
Collected about 1.5 million kilometers’ real-road data by 3-6 months of stable driving.
Data Survey for HDV
Based on collected data, determine typical scenes that are prone to generate noise. Establish corresponding test projects in the standard system.
Based on scene information, calculate statistical characteristics to design specific test methods and conditions.
4

## Slide 5
Data Survey for HDV (Speed & Engine Speed)
Engine Speed ( Rated：1900rpm） |  |  |  |  | 
Percentile （Time） | 50% | 80% | 90% | 95% | 99%
50 | 1142 | 1300 | 1355 | 1397 | 1470
Percentage | 60.1% | 68.4% | 71.3% | 73.5% | 77.4%
80 | 1519 | 1575 | 1615 | 1637 | 1683
Percent | 79.9% | 82.9% | 85.0% | 86.2% | 88.6%
Acceleration Percentile(m/s2) |  |  |  |  | 
50 | 0.14 | 0.25 | 0.33 | 0.42 | 0.61
80 | 0.08 | 0.14 | 0.19 | 0.25 | 0.44
Distributions: Blue-time, orange-distance.
The test methods here are quite different from current test methods.
The methods are designed firstly by speed range and then other parameters are considered.
5

## Slide 6
GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions”
Vehicle Type | Testing Driving Mode Conditions |  |  | 
 | Starting | Low-Speed Acceleration | Mid-Speed Cruise | High-Speed Cruise
Tractor | √ | √ | √ | √
Dumper | √ | √ | √ | ——
Truck | √ | √ | √ | √
Bus | √ | √ | √ | ——
Coach | √ | √ | √ | √
1. Dumpers and Buses do not take the High-Speed Cruise test. 2.“√”: the test is required，“——” the test is not required. |  |  |  | 
6

## Slide 7
GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions”
Starting condition test Lstart
Start the vehicle, wait for the engine speed or power system to stabilize, measure the maximum "A" weighted sound pressure level (Unloading sudden noise of compressed air system is not included).
Low-speed acceleration test Llow acc
vtest: 30 km/h ±2km/h, ntest≤90％S
Gear selection (if possible): can be accelerated steadily, within the vtest range and ntest range, ntest as high as possible.
Mid-Speed Cruise
test Lmed cru
vtest: 50 km/h ±2km/h, ntest≤80％S*
Gear selection (if possible): can be accelerated steadily, within the vtest range and ntest range, Gear as high as possible.
High-Speed Cruise
test Lhigh cru
Vtest: 80 km/h ±2km/h, ntest≤80％S*
Gear selection (if possible): can be accelerated steadily, within the vtest range and ntest range, Gear as high as possible.
* If it is limited by the maximum speed, acceleration performance of the test vehicle and measurement site, the test target speed can be adjusted appropriately and noted in the test report.
7

## Slide 8
GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions”
Vehicle Type |  | Weighting coefficient ki* |  |  | 
 |  | Starting weighting coefficient kstart | Low speed acceleration weighting coefficient klow acc | Mid-speed cruise weighting coefficient kmed cru | High-speed cruise weighting coefficient khigh cru
Speed Range (km/h) |  | 0-10 | 10-35 | 35-60 | 60+
Tractor |  | 18.2% | 20.3% | 14.9% | 46.6%
Dumper |  | 36.2% | 34.6% | 29.2% | --
Truck | （GVW≤5 500 kg） | 26.3% | 29.7% | 23.3% | 20.7%
 | （GVW＞5 500 kg） | 26.6% | 26.7% | 26.8% | 19.9%
Bus |  | 44.9% | 44.0% | 11.1% | --
Coach |  | 28.8% | 21.0% | 22.0% | 28.2%
* Derived from the time accumulation survey results.
8

## Slide 9
GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions”
i : driving mode conditions number（i =1, 2, 3, 4）
ki : weighting factors kstart, klow acc, kmed cru, khigh cru
Li: noise result Lstart , Llow acc , Lmed cru , Lhigh cru
9

## Slide 10: Conclusions
10
GB/T “Measurement Methods for Noise Emitted by Heavy-duty Vehicles in Multiple Driving Mode Conditions” is soliciting public opinion.
30 km/h±2km/h, 50 km/h±2km/h, 80 km/h±2km/h are three typical speed ranges.
Starting, low-speed acceleration, mid-speed cruise, high-speed cruise testing are with different target vehicle speed, engine speed and gears.
A consolidate noise result was calculated according to the time accumulation, reflecting the real influence of HDVs.

## Slide 11
Thanks for your attention!
China Automotive Technology and Research Center Co., Ltd..
11