## Slide 1
Improved failure provisions for UN R149-01 and including “high definition” headlamps
- Main aspects of the approach -
88th GRE session, 25-28 April 2023
-GTB/ WG-FL (Front lighting)-
Informal document GRE-88-10
(88th GRE, 25-28 April 2023, agenda item 7)

## Slide 2
Improved failure provisions of “high definition” headlamps
Motivation
While new technologies and light sources are available, we now have dipped-beam headlamps constituted of a large number of light-emitting elements where a failure of any first of these does not lead to an essential change of performance in photometric values.
Considering the current regulatory text in UN R48, the failure requirements for principal dipped-beam headlamps using multiple light sources are quite simple and state very generally that, every failure of a LED module shall lead to either switching OFF the LED module(s) of the principal dipped-beam or activating a tell-tale indicating failure.
Failure of one LED module  considerable loss of dipped-beam performance
-GTB/ WG-FL (Front lighting)-

## Slide 3
Improved failure provisions for UN R149-01 and including “high definition” headlamps - Details of the concept
For principal dipped-beam headlamps in UN R48:
the existing requirements are kept and apply to devices type-approved according to UN R112 or to the original series of amendments to UN R149;
existing requirements are adapted for failure detection at vehicle level to suit devices type-approved according to UN R149 01 series;
a new option is added for the principal dipped-beam headlamps type-approved according to the 01 and subsequent series of UN R149, if there is a failure signal provided by the device.
At device level, for UN R149-01 series:
insertion of detailed provisions for providing a failure signal, based on different technologies
UN R48
Failure detected by vehicle
 extended provisions
UN R149 01 series
Failure detected by device
 new detailed provisions
-GTB/ WG-FL (Front lighting)-

## Slide 4
New detection possibilities intended to be offered in R149-01
Improved failure provisions of “high definition” headlamps
Details of the concept – new provisions UN R149-01 series
Manufacturer shall choose at least one criterion depending on the diagnosis technology to provide a failure signal
First element failure
Luminous flux
Legal values
Number of failed elements
Any first light source or light-emitting element fails
> 5 % flux loss of a specific function
Adaption of the current provision for light sources
> 5 % of the overall number of light-emitting elements failed
Low value to avoid negative impact on traffic safety and to minimize the probability of dark holes
Luminous intensity
< 80% of any minimum requirement
20% tolerance corresponds to the Conformity of Production criteria
Low value to avoid negative impact on traffic safety and to minimize the probability of dark holes
-GTB/ WG-FL (Front lighting)-