## Slide 1: Generic Vehicle Models for MR1
SUV
Familycar
Roadster
Informal document GRSP-73-59 (73rd GRSP, 15-19 May 2023 agenda item )

## Slide 2: Overall DPPS Process
4. DPPS decision for tests
3. Head Impact Time vs. WAD determination
2. HBM qualification with GV
1. GV Plausibility check
Chart: 
max Defl | 0 | 10
OK
Impactor corridors
GV Models
HBM corridors
GV Models + HBM
DPPS vehicle + HBM
HIT vs. WAD graph
Static test / dynamic HIT
OK

## Slide 3: Building Blocks
Finite Element Software
(supplied by code-houses to Industry)
Generic Vehicle Models
available on UNECE website – MR1
Human Body Models (openly available or by suppliers)
Vehicle Simulation Models of vehicle with DPPS of Vehicle Manufacturer
2. Human Body Model qualification
1. Plausibility check
3. HIT vs. WAD determination
SUV
Familycar
Roadster
4. Use HIT for
DPPS decision

## Slide 4: What are Generic Vehicle Models?
FE Code | Unit System | Master files | File ID
LS-Dyna | mm, kg, ms | GV_FCR_R3_1_mm_kg_ms.key | D-GV-1
 |  | GV_RDS_R3_1_mm_kg_ms.key | D-GV-2
 |  | GV_SUV_R3_1_mm_kg_ms.key | D-GV-3
 | mm, to, s | GV_FCR_R3_1_mm_to_s.key | D-GV-4
 |  | GV_RDS_R3_1_mm_to_s.key | D-GV-5
 |  | GV_SUV_R3_1_mm_to_s.key | D-GV-6
RADIOSS | mm, kg, ms | GV_FCR_R3_1_mm_kg_ms.0000.rad GV_FCR_R3_1_mm_kg_ms.0001.rad | R-GV-1 R-GV-10
 |  | GV_RDS_R3_1_mm_kg_ms.0000.rad GV_RDS_R3_1_mm_kg_ms.0001.rad | R-GV-2 R-GV-20
 |  | GV_SUV_R3_1_mm_kg_ms.0000.rad GV_SUB_R3_1_mm_kg_ms.0001.rad | R-GV-3 R-GV-30
 | mm, to, s | GV_FCR_R3_1_mm_to_s.0000.rad GV_FCR_R3_1_mm_to_s.0001.rad | R-GV-4 R-GV-40
 |  | GV_RDS_R3_1_mm_to_s.0000.rad GV_RDS_R3_1_mm_to_s.0001.rad | R-GV-5 R-GV-50
 |  | GV_SUV_R3_1_mm_to_s.0000.rad GV_SUV_R3_1_mm_to_s.0001.rad | R-GV-6 R-GV-60
VPS | mm, kg, ms | GV_FCR_R3_1_mm_kg_ms_VPS.inc | V-GV-1
 |  | GV_RDS_R3_1_mm_kg_ms_VPS.inc | V-GV-2
 |  | GV_SUV_R3_1_mm_kg_ms_VPS.inc | V-GV-3
 | mm, to, s | GV_FCR_R3_1_mm_to_s_VPS.inc | V-GV-4
 |  | GV_RDS_R3_1_mm_to_s_VPS.inc | V-GV-5
 |  | GV_SUV_R3_1_mm_to_s_VPS.inc | V-GV-6
Human readable text files
interpreted by the different FE software
no executables (software)

## Slide 5: How does a GV Model file look like? Example:
*KEYWORD
$*******************************************************************************
$ FILE ID: D-GV-1 *
$ *
$ DESCRIPTION: *
$ *
$ Generic Vehicle Models for the qualification of Human Body Models *
$ as described in M.R.1 - Mutual Resolution No. 1 of the 1958 and the 1998 *
$ Agreements ECE/TRANS/WP.29/1101 Addendum 5 *
$ *
$ ==========
$ NODE cards
$ ==========
$
*NODE
1000000 -116.12 -587. 224.81
1000101 -262.54999 -587. 701.16998
1000102 -252.04385 -579.58826 701.16998
1000103 -243.27393 -579.58801 692.83368

## Slide 6: Differences between Dummies and GV Models in Mutual Resolution 1 (MR1)
Crash-test Physical Dummies
Drawings specified in MR 1
  products purchased at suppliers
Certification specified in MR1.
  If not fulfilled, replacement parts will be purchased at suppliers.
Not sensitive to the lab environments they are used within specified conditions.
Issues with specific Dummies reported to suppliers.
  General issues with dummies are reported to GRSP by CP or NGOs
Generic Vehicle Models
Directly provided by UNECE
  Downloaded from website
Certification specified in MR1.
  If not fulfilled, OEM can change this model. However, this should be avoided as much as possible to ensure comparability of the models.
Simulation models are sensitive to the simulation environment they are used in.
Issues to be collected dynamically
  depend on simulation environment
  need to be addressed in updated versions of GV models

## Slide 7: Proposal for reporting and technical support
Who is the contact for users if they encounter issues in the usage?
  UN Contact form for technical support on Generic Vehicle Models
    forwarded to Austrian experts
How to ensure that any issues are addressed in updated versions of the GV models?
  clarify in MR1 that any identified issues which require changes + the required changes must be reported to GRSP through a Contracting Party

## Slide 8: Draft of MR1 GRSP-73-10e_rev1
4.1. The certification of Impactor simulations on the generic vehicle models may be performed if the user has any doubt that the generic vehicle models work properly with the solver version and control cards used as plausibility check. If issues (i.e. significant the deviations to the reference curves outside of the provided corridors shown in red) are identified, the user shall switch to another solver version, [and] review the control settings [and report the issue to gv.vsi@tugraz.at. GRSP through a Contracting Party].
4.4. If modifications of the models are required, they shall comply with the specified corridors and be documented and reported to [GRSP through a Contracting Party].

## Slide 9: Copyright of GV Models
All stakeholders (funding Organisations & Contributors) of GV models have formally agreed (signed) confirmations to enable usage and upload of GV models by UNECE
Letter by Graz University of Technology on its way