## Slide 1: Report to 78th Session of GRBP (August/September 2023)
Special Interest Group Automated Vehicles Regulation Screening
(SIG AVRS)
Transmitted by Chair of SIG AVRS
Informal Document GRBP-78-24
78th GRBP, 30th August- 1st September 2023,
agenda item 13

## Slide 2: SIG Automated Vehicles Regulation Screening
7
12
Number of Meetings
Web-meetings
1st SIG AVRS: 7th December 2022
2nd SIG AVRS: 18th January 2023
3rd SIG AVRS: 2nd June 2023
4th SIG AVRS: 19th June 2023
5th SIG AVRS: 28th June 2023
6th SIG AVRS: 14th July 2023
7th SIG AVRS: 26th July 2023
Guidance meetings with GRVA FADS
April/June 2023
CPs: Germany, China, Japan, The Netherlands
NGO‘s: OICA
Participants (Contracting Parties & NGOs)

## Slide 3: SIG Automated Vehicles Regulation Screening
WP.29 requests a screening of regulation for application of Automated Vehicles.
GRVA proposed a template for the screening
TF-FADS (GRVA) provides further guidance
Targets
Chair: Netherlands
Secretariat: OICA
Roles
https://wiki.unece.org/pages/viewpage.action?pageId=190087308
SIG AVRS wikipage
Documentation:
Report of the World Forum for Harmonization of Vehicle Regulations on its 187th session pg.8/9
19. AC.2 received an update on the work of GRVA and automated vehicles related activities:
(e) AC.2 recommended the GRs to consider using the template in GRVA-13-18 when screening UN GTRs and UN Regulations with regards to ADS.
Reference:
https://unece.org/sites/default/files/2022-07/ECE-TRANS-WP29-1166e_0.pdf
https://unece.org/sites/default/files/2022-05/GRVA-13-18e.pdf
Report GRVA FADS from WP.29 June 2023: https://unece.org/sites/default/files/2023-06/ECE-TRANS-WP.29-2023-86e.pdf
Report WP29 190th meeting, June 2023: https://unece.org/sites/default/files/2023-07/ECE_TRANS_WP.29_1173e_0.pdf items 25 to 32.

## Slide 4: Summary of earlier work
21 regulations screened
13 regulations for further consideration
GRBP decides to start with first detailed assessment of prioritized regulations
  R9, R28, R51, R138, R165
(Sub)categories of AVs are not defined yet

## Slide 5: Developments
Under GRVA guidance
  Report for all GR’s and regulations to be assessed with priority
  Proposal accepted in WP.29 June 2023
GRVA-16-13 document with proposal for subcategories (OICA/CLEPA)
  Needs further detail and confirmation in R.E.3 (expected in oct. 2023)
  Some category letters are already in use, new definition needed

## Slide 6
Vehicle categorization under R.E.3
N2
N3
M2
M3
M1
M3A
M2A
M1A
N2A
N1A
M1D
N3D
Subcategory D
„Dual Mode vehicles“
N1
GVM </= 3.5t
3.5t < GVM </= 12t
GVM > 12t
M2X
< [25] km/h
e.g. Hub-2-Hub truck
e.g. Robotaxi
Subcategories X & Y
„Low speed driverless AV‘s“
M2Y
[25] km/h </= v </= [50]
e.g. Urban shuttle
e.g. Campus shuttle
GVM </= 3.5t
3.5t < GVM </= 12t
GVM > 12t
Designed primarily for the carriage of people
Designed primarily for the carriage of goods
Driver seat + max. 8 add. seats, no limitation of GVM
Driver seat + more than 8 add. seats, GVM max. 5 t
Driver seat + more than 8 add. seats, GVM exceeding 5 t
Vehicles which can be driven manually under nominal conditions
AV‘s which do not require a driver/fallback-ready user
New sub categories for Automated Vehicles (AV‘s)
N3A
*Class I, II, III and Class A, B can be carried over
M1Z
e.g. AVP equipped vehicle
Designed primarily for the carriage of people
Designed primarily for the carriage of goods
With or w/o passengers
More than 9 seats or standing passengers, GVM Max. 5t
seated only, max. 9 seats
More than 9 seats or standing
passengers, GVM exceeding. 5t
Subcategory A „Driverless Vehicles with ADS“
Examples:
Examples:

## Slide 7: General principle
Approach for amendments
  Scope
  Definitions
    Incl. type definitions
  Specifications
  Test method
  Each with justification to support understanding and considerations of the group
Use-cases will be discussed in the GRVA-FADS
  Verify the usefulness of test and regulation for the use-case
  Exemptions for AV’s in GRBP Regulations for special use-cases

## Slide 8: First discussion on R51
General
  R51 test method can be adopted for AVs
  Are R51 formal aspects, limits and testing suitable for AVs?
    Use-case specific (city shuttles, robotaxi, delivery robot) exemptions and adoptions might be necessary.
    This needs input from GRVA/industry
Subcategory approach and exempt specific subcategories
  Exact definition of categories is pending (R.E.3)
Dual mode discussion
  Needs further refinement
  Try to use the existing test method in manual mode

## Slide 9: First discussion on R138
General
  R138.02 could typically be used for AVs
    Existing requirement in R138 (Scope) allows also non-audible solutions1
    Test methods (simulated speed) fits very well
  Are R138 limits and testing suitable for AVs?
    Is AVAS still needed for the safety level of AVs?
    First impression is: Yes, but it could be more limited to specific situations (only for areas with interaction with pedestrians, “uncontrolled” situations, etc). “Smart AVAS”.
    Use-case specific
Subcategory approach and exempt specific subcategories
  Exact definition of subcategories probably based on use-cases is pending (R.E.3),
Dual mode (automatic/manual like R157 ALKS)
  Needs refinement
  Special test mode = simulated speed signal
Test methods would work for AV
1) At this stage, only acoustic measures shall be developed in order to overcome the concern of reduced audible signals from electrified vehicles. After finalization, the appropriate GR shall be assigned with the enhancement of the Regulation in order to develop alternative, non-acoustic measures, taking into account active safety systems such as, but not limited to, pedestrian detection systems. To provide for environmental protection, this Regulation specifies also maximum limits.

## Slide 10: Dependencies
Vehicle subcategories will be updated (GRSG R.E.3)
Use-cases should relate to subcategories
Input from GRVA for requirement in GRBP regulations
  Concept of Communication/Warning needed

## Slide 11: Next steps
Regulations with first priority (based on priority and capacity of the group)
R28 (postponed)
R51
  Definitions will be aligned with GRVA
  Dual mode can be added when assumed that the manual mode is the loudest
R138
  Start in September 2023 after draft text of R138.02
  R138.02 (jan. 2025) can probably be used with minor changes
We expect slow progress due to complexity of the subject and dependencies.
  R.E.3 update by GRSG
  Feedback of GRVA
  All changes before end of 2025 need to be in a supplement

## Slide 12: Thank you for your attention

## Slide 13: Next slides are background from GRBP-77

## Slide 14: Screening process: Presumptions
1. Availability of manual driven vehicles was assumed for component (tyres) testing
2. Categories of AVs are not defined yet
  Excluding an AV-category is not possible yet
  AV-categories could be useful
3. Automation of Powered 2 Wheelers is unlikely, but prototypes exist.
  L1/L3 is not excluded
  Priority could be “LOW”

## Slide 15: Screening process: Considered items
Terminology and concepts
Relevance of regulation for AVs
  The subject of the regulation is relevant to the AVs
  The test method needs reconsideration for AVs
    For driverless AVs (Level 5, shuttles)
      With passenger
      Without passengers (cargo)
    For AVs with driver (Level 3/4, fallback driver/user)
    Bi-directional AV’s
Requirement to AVs to fulfill Regulation that is screened.

## Slide 17
TCI-model Task Capability Interface Model (Simplified) Fuller, 2000 For reference and to explain complex traffic situations
AV control
For reference